## Slide 1: DA4 – Fractional Numbers
COMP 256 – Dickinson College
Prof. Braught
Spring 2023
Notes: Fractional or non-whole numbers
- 12.34
- 3.14
- -29.93
Etc…

## Slide 2: Fixed Point Values
What is the base 10 value of this unsigned Fixed Point binary number?
= 2*102 + 1*101 + 9*100 . 7*10-1 + 5*10-2
= 2*100 + 1*10 + 9*1 . 7*1/10 + 5*1/100
219.7510
= 2*100 + 1*10 + 9*1 . 7*0.1 + 5*0.01
110.1012XP
Decimal
Point
Binary
Point
Notes: Fixed Point
- There are some number of digits to the left and right of the decimal point.
We will use 2XP as the subscript to indicate binary fixed point.
We call the . the decimal point in base 10
In base 2 we call it the binary point.

## Slide 3: Fixed Point Values
What is the base 10 value of this unsigned Fixed Point binary number?
= 2*102 + 1*101 + 9*100 . 7*10-1 + 5*10-2
= 2*100 + 1*10 + 9*1 . 7*1/10 + 5*1/100
219.7510
= 2*100 + 1*10 + 9*1 . 7*0.1 + 5*0.01
110.1012XP
Binary
Point
Decimal
Point
= 1*22 + 1*21 + 0*20 . 1*2-1 + 0*2-2 + 1*2-3
= 1*4 + 1*2 + 0*1 . 1*0.5 + 0*0.25 + 1*0.125
= 4 + 2 + . 0.5 + + 0.125
= 6 . 0.625
= 6.62510
Notes: Worked out solution to the previous slide.

## Slide 4
Find the 6-bit unsigned Fixed Point binary representation for the given base 10 number.
Use 3-bits to the right of the binary point.
5.37510
= .
22 21 20 2-1 2-2 2-3

## Slide 5
Find the 6-bit unsigned Fixed Point binary representation for the given base 10 number.
Use 3-bits to the right of the binary point.
5.37510
= .
22 21 20 2-1 2-2 2-3
= 1 0 1 .
4 2 1 2-1 2-2 2-3
= 1 0 1 . ___
4 2 1 0.5 0.25 0.125
= 1 0 1 . 0 1
4 2 1 0.5 0.25 0.125
0.375
-0.25
0.125
-0.125
0.0
= 1 0 1 . 0 1 1 2XP
4 2 1 0.5 0.25 0.125

## Slide 6
How might we represent 2.410 in 4-bit unsigned Fixed Point binary with 2 bits to the right of the binary point.
2.410 ≈
. 2XP
21 20 2-1 2-2
Notes: Give it a shot…
What happens?
What might we do about it?

## Slide 7: Precision Errors
Some values will not be able to be represented exactly in the number of bits available.
  These situations, result in what are called precision errors (i.e. rounding errors).
Under Estimate The next smaller representable number.
Over Estimate
The next larger representable number.
How might we represent 2.410 in 4-bit unsigned Fixed Point binary with 2 bits to the right of the binary point.
2.410 ≈
= 2.2510
1 0 . 0 1 2XP
21 20 2-1 2-2
2.410 ≈
or
1 0 . 1 0 2XP
21 20 2-1 2-2
= 2.510
Notes: Once we pick a number of bits to be used not all fractional parts will be able to be represented.
- We can choose to represent 2.4 as
- 10.01 = 2.25
- or as
- 10.10 = 2.5
- But given the number of bits we have we cannot represent it exactly.
- This is called a precision error.
- Or you might call it a rounding error as the value is rounded off.
For any value we cannot represent exactly
- we will can create an under estimate and an over estimate.
- under estimate
- is the next smaller value we can represent
- it is as close as possible without going over.
- over estimate
- is the next larger value that we can represent
- as close as possible without going under.
Our normal process of subtracting from the value being represented
- Will give an underestimate
- there will still be some value left to represent when we run out of bits.
- Add 1 to LSbit with carries to get the over estimate.
If we have more bits, we’ll get different estimates.
Typically, programs will use whichever estimate is closest.*
- So we would use 2.5 here.
- * Approximately
- take MATH/COMP 241 or
- do some reading on the IEEE 754 Standards

## Slide 8: Precision Errors
A precision error occurs when there are insufficient bits to the right of the binary point to represent a value exactly.
Example:
Image From: https://www.exploringbinary.com/why-0-point-1-does-not-exist-in-floating-point/
0.110 ≈
System.out.println(101.0 * 0.1);
➜ 10.100000000000001
Try it: https://replit.com/@braughtg/PrecisionError
Notes: Why does this happen?
- We know 101.0 can be represented because it has no fractional part.
- But the 0.1?
- If we could get 0.1 exactly
- then multiply we should get 10.1
- So 0.1 is the culprit… and its an interesting one…
- it turns out that 0.1 cannot be represented exactly in binary with any number of bits.
- Given some number of bits we will always have to over estimate or under estimate.
- Adding more bits will let us get closer and closer, but the problem does not go away.
At whatever point we cut it off…
- e.g. 52 bits for a double value in the IEEE 754 standard that is typically used.
- there will be a precision error (or rounding error).

## Slide 9: Scientific Notation
In decimal we can represent very large and very small numbers compactly using scientific notation.
3,193,000,00010
0.0000074210
= 3.193 x 109
= 31.93 x 108
= 0.003193 x 1012
= 7.42 x 10-6
= 742.0 x 10-8
. . .
. . .
= 3.193E9
Notes: Computers usually use the E notation.
There are lots of equivalent representations.
- Notice that we move the decimal point and adjust the exponent up or down accordingly.
- Each position we move the decimal is one more or less on the exponent.
- multiplying or dividing by 10.
We can do the exact same thing with binary…

## Slide 10: Scientific Notation in Binary
Scientific notation (i.e. floating point) works equally well with binary numbers. Just change the base to 2.
1011.001112XP
= 1.01100111 x 23
= 10110011.1 x 2-4
. . .
= 1011.00111 x 20
= 10110.0111 x 2-1
= 101.100111 x 21
Notes: Again lots of equivalent representations.
Every move of the binary point is multiply or divide by 2.
Floating point: the point ”floats around”
- this is where the datatype name float comes from in Java and other languages.

## Slide 11: Normalized Forms
The normalized form of a number in scientific notation has exactly one significant (non-zero) digit (or bit) to the left of the decimal (or binary) point.
23793.1310 = 2.379313 x 104
0.00329810 = 3.298 x 10-3
1001000.01102XP = 1.0010000110 x 26
0.01011012XP = 1.01101 x 2-2
Notes: Notice that while there are many different ways to write the same number in scientific notation
The normalized form is unuique.
- There is only one normalized form for each number.
This uniqueness is critical to representing the value in binary
- We can’t write the . (because we only have 0’s and 1’s)
- So we need some way to know where it is
- With normalized form we always know where it is!
- It is to the right of the first digit or bit.

## Slide 12: A 14-bit Floating Point Representation
  Sign: 0 - Positive, 1 - Negative
  Exponent: Two’s Complement Representation
  Significand: The bits of the number in normalized form.
+ 1.0101 101 x 24
Notes: We are going to see how to represent numbers like this one…
- In normalized binary scientific notation using 14 bits.
- In most computers today
- float uses 32 bits
- double uses 64 bits
- newer standards also define quadruple and octuple precision with 128 or 256 bits.
- We do it with 14 to keep it manageable to do examples by hand.
- So we can learn the concepts involved.
We divide the 14 bits into fields
- one for the sign
- 5 to represent the exponent on the 2
- 8 to represent the bits in the number.
Sign – just like sign magnitude
Exponent – we will use 2’s complement
- let’s us have both positive and negative exponents.
- modern computers do it a little different.
Significand – in normalized form.
Given a 14 bit floating point number
- we divide it into its fields
- and use the formula here to compute its base 10 value.
The formula is the same as at the top just rearranged.
- Note: -10 = 1 and -11 = -1
- so this is just clever way of working the sign into the equation.
- Exponent is the power of 2
- multiply by the value of the bits.

## Slide 13: 14 Bit Floating Point Example
Binary to Decimal
1 00101 1001 10102FP-14
Notes: Let’s do an example.
Steps:
1. Start from the formula
2. Insert the sign, exponent and significand bits.
- add the binary point to the significand.
3. Convert the sign to +1 or -1
4. Convert the exponent to base 10 using two’s complement representation
5. Convert the significand to base 10 using fixed point representation
6. Work out the final value.

## Slide 14: 14 Bit Floating Point Example
Decimal to Binary
13.562510
Note: 2-4 = 0.062510
= 0 00011 110110012FP-14
Notes: An Example the other way around:
Steps:
1. Make the sign explicit (+1 or -1)
2. Convert the base 10 value to fixed point using the right number of bits (8 here)
- 13 = 1101
- 0.5625 = 0.5 + 0.0625
- This fits in 8 bits, but may need to round if it does not.
3. Normalize the significand and determine the exponent in base 10
- Moved the binary point 3 places left
- So exponent is 3
4. Convert the exponent to 5-bit two’s complement.
- 3 = 00011
5. Figure out the sign bit (0 or 1)
- -1^0 = +1
6. Place the bits into the correct fields
- drop the binary point.

## Slide 15: Floating Point Errors
A precision error is when a value in the expressible range cannot be represented exactly and must be rounded.
An overflow error is when a value is out of range. It is too positive or too negative to be represented in the number of bits being used (same as whole numbers)
An underflow error is when a result is too close to zero to be represented in the number of bits being used.

## Slide 16: Floating Point Optimizations
In practice Floating Point operations are optimized.
  Implied bit
  Denormalized forms
  Excess representation for exponent
COMP/MATH 241 – Computational Mathematics
Notes: If there is time mention these.
Otherwise just leave them out.
You will learn a little about some of these optimizations in the Activities.
- They provide
- a larger range of values (implied bit / denormalized form)
- greater control over precision (excess representation)
COMP/MATH 241 if you want to know it all.

## Slide 17: Acknowledgments
https://creativecommons.org/licenses/by/4.0/
Slide Template From:
Slide Content Licensed as:
Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.
Notes: Note: Individual images may be covered by their own licensing agreements and were incorporated here under fair use. Their use in this slide deck does not change or alter their licensing.

## Slide 18: Fixed Point Binary Representation
Binary to Decimal Conversion
110.1012XP
= 1*22 + 1*21 + 0*20 . 1*2-1 + 0*1-2 + 1*2-3
= 1*4 + 1*2 + 0*1 . 1*0.5 + 0*0.25 + 1*0.125
= 4 + 2 + . 0.5 + + 0.125
= 6 . 0.625
= 6.62510
Binary
Point
Notes: 2xp for – Fixed Point

## Slide 19: Fixed Point Decimal Numbers
Extending binary representation to include fractional numbers is also analogous to decimal numbers.
Example:
19.7510
= 1*101 + 9*100 . 7*10-1 + 5*10-2
= 1*10 + 9*1 . 7*0.1 + 5*0.01
= 10 + 9 . 0.7 + 0.05
= 19 . 0.75
= 19.7510
Notes: I like to process the parts of the number to the left and right of the decimal point separately.
Write it with decimal point until the last step.
Then add them up and get the full value.
Will do the same thing when we go to binary.

## Slide 20: Fixed Point Binary Representation
Decimal to Binary Conversion
  6-bit fixed point, with 3 bits to the right of the binary point.
5.37510
= _*22 + _*21 + _*20 . _*2-1 + _*2-2 + _*2-3
= _*4 + _*2 + _*1 . _*0.5 + _*0.25 + _*0.125
= 1*4 + 0*2 + 1*1 . _*0.5 + _*0.25 + _*0.125
= 1*4 + 0*2 + 1*1 . 0*0.5 + 1*0.25 + _*0.125
0.375
-0.25
0.125
= 1*4 + 0*2 + 1*1 . 0*0.5 + 1*0.25 + 1*0.125
-0.125
0.0
= 101.0112XP
Unsigned
Binary
Notes: When working with fixed point you will know
- the number of bits and
- the number of bits to the right of the binary point.
Left of the binary point – old hat… just unsigned binary

## Slide 21: Precision Errors
Represent 2.4 using 4-bit fixed point with 2 bits to the right of the binary point.
2.410 ≈ 10.012XP = 2.2510
2.410 ≈ 10.102XP = 2.510
or
Under Estimate – the next
smaller representable number.
Over Estimate – the next larger representable number.
As close as possible without going over.
Notes: Once we pick a number of bits to be used not all fractional parts will be able to be represented.
For any value we cannot get exactly right we will be able to produce an under estimate and an over estimate.
- under – as close as possible without going over.
- over – as close as possible without going under.
Note that if we add more bits to the right of the binary point these estimates will change.
- Just have to fiddle with them to figure out what I closest without going over or under.
- There are algorithms, but beyond what I want to get into in this class.

## Slide 22: Rounding Modes
When there is a precision error in representing a value, rounding is used to determine its representation.
There are different rounding modes and each will use either the over estimate or the under estimate:
More to this: Take MATH/COMP 241 – Computational Mathematics
Notes: Up – take the more positive value.
Down – take the more negative value
Zero – take the value closer to zero
To Nearest – figure out the over estimate and the under estimate and take the closer one
- This is typically what is used by default in your programs
- with a few small adjustments to mitigate accumulation of errors.
- Math/COMP 241 – all the gory details.
But most programming languages will allow you to change which rounding mode is used.
Different modes may have different purposes,
- For example,
- If we are calculating the signal to send to rocket thruster
- If we go over then the thruster will explode
- So, we would want to be sure to use round down!
Notice that I’ve cheated a bit and just used a – sign here.
We’ll resolve that in a moment.

## Slide 23: A 14-bit Floating Point Representation
  Sign: 0 - Positive, 1 - Negative
  Exponent: Two’s Complement Representation
  Significand: The bits of the number in normalized form.
Notes: We are going to make some simplifications from how this is actually done.
Let’s us focus on the critical ideas rather than getting hung up on the more complicated optimizations that are made in practice.
Exponent in 2’s complement let’s us have both positive and negative exponents.