## Slide 1: 11 – The Stored Program Architecture
COMP 256 – Dickinson College
Prof. Braught
Spring 2022
Notes: The stored program architecture is the big idea around the way the K&S and all other computers you use are organized.
- We’ll come back to it at the end of the class.
- At that point we’ll already understand what the stored program architecture is.
- We will just give some things names and place what we know into that framework.
First, want to look at a little more of how the K&S works…

## Slide 2: K&S Machine Language Programming
What operations would a machine language program for the K&S computer need to do to perform the following computation: MM[20] = absolute value of MM[19]
Operation
Notes: A little warmup and motivation for today’s topic…
Easy to start:
- move MM[20] into a register…
- But then what?
A little bit of a trick question…
- What’s the problem?

## Slide 3: Branching
for (j=0; j < 10; j++) {
<code>
}
while (i >= 0) {
<code>
}
if (x < 0) {
y = -x;
}
else {
y = x;
}
A branch changes the flow of the program.
Notes: The issue is that to compute the absolute value
- You need to do one thing under one condition
- and something else under another condition.
We would typically express that using an if/else statement in a high level language like Java.
- Under one condition (x < 0) we just go to the next instruction
- Under a different condition (x >= 0) we jump to a different instruction.
We’ll call this “branching”
- Branching allows the program to not simply go one instruction after the next
- It makes it possible to jump (i.e. branch) to other instructions
- Possibly based on conditions.
Some other examples:
- while loop and for loop
- branch over the loop body,
- or jump back to the top of the loop.

## Slide 4: Branching
Under what condition is each of these branches taken?
while (i >= 0) {
<code>
}
if (x < 0) {
y = -x;
}
else {
y = x;
}
A branch changes the flow of the program.
Branches are conditional or unconditional.
for (j=0; j < 10; j++) {
<code>
}
Notes: - Conditional branches
- A conditional branch is one that may or may not be taken
- If the branch is taken
- the flow of the program changes
- i.e. the program jumps to an instruction that is not the next one.
- If the branch is not taken
- the program simply goes onto the next instruction.
- Just like we had seen previously when it ran one instruction after the other.
The conditional branch points are pretty easy to spot.
And the locations to which they branch should make sense based on our understanding of high level language constructs.
Now notice the definition… a branch changes the flow of the program.
- That is the program does not go to the next instructions.
- So under what condition are these branches taken?
- Think carefully…

## Slide 5: Branching
for (j=0; j < 10; j++) {
<code>
}
if (x < 0) {
y = -x;
}
else {
y = x;
}
A branch changes the flow of the program.
Branches are conditional or unconditional.
Under what conditions are these branches taken?
x >= 0
i < 0
j >= 10
while (i >= 0) {
<code>
}
Notes: Notice that conditions for taking each branch is inverted from what we normally write in a high level language like java.
For example:
- If
- when x > 0 the branch is taken, and the program jumps to the else.
- when x <= 0 the branch is not taken, and the program just goes onto the next instruction.
- while
- when i < 0, the branch is taken, and the program jumps to the end of the loop
- when i >= 0 the branch is not taken, and the program just goes to the next instruction.
- for
- when j >= 10, the branch is taken, and the program jumps to the end of the loop.
- when j < 10, the branch is not taken, and the program just goes to the next instruction.

## Slide 6: Branching
for (j=0; j < 10; j++) {
<code>
}
while (i >= 0) {
<code>
}
if (x < 0) {
y = -x;
}
else {
y = x;
}
Where are the unconditional branches and to where to they branch?
A branch changes the flow of the program.
Branches are conditional or unconditional.
Notes: An unconditional branch is always taken.

## Slide 7: Branching
A branch changes the flow of the program.
Branches are conditional or unconditional.
for (j=0; j < 10; j++) {
<code>
}
while (i >= 0) {
<code>
}
if (x < 0) {
y = -x;
}
else {
y = x;
}
Where are the unconditional branches and to where to they branch?
Notes: An unconditional branch is always taken.
If
- at the end of the if body
- an unconditional branch is used to jump over the else body.
While
- at the end of the loop body
- an unconditional branch is used to jump back to the top of the loop.
- then the condition is checked again.
For
- at the end of the loop body
- an unconditional branch is used to jump back to the “update” (e.g. j++) part of the loop.
- then the condition is checked again.

## Slide 8: Branching
How can the machine change which instruction is executed next?
How can it be conditional?
Notes: If programs are going to branch, and most interesting ones will need to…
It is necessary that the hardware on which the program is running be able to make it happen…
Turns out, we already have the parts we need.
Can you figure out what they are and how they are used?

## Slide 9: Branching
How can the machine change which instruction is executed next?
How can it be conditional?
Notes: Recall:
- The Program Counter PC determines the memory address from which the next instruction is fetched
- I.e. The instruction at MM[PC] is the next one that is moved into the Instruction Register (IR)
- So if an instruction that is executing can change the PC then we can branch.
- That simple.
- Notice the Arrow from the Instruction Interpretation Unit to the PC
- That indicates that this unit can change the PC.
- So, some instructions (and we’ll see them in a moment) can change the PC.
To make the branching conditional:
- The ALU flags are useful.
- Zero – is set when the last ALU result was zero.
- Negative – is set when the last ALU result was negative in two’s complement.
- Two others for overflow that we pretty much will ignore.
- But are interesting if you want to delve more into understanding overflow.

## Slide 10: Branching in the K&S Machine Language
0000 0010 000
xxxxx
If Zero PC ← MM
MM
Branching Instructions
0000 0011 000
xxxxx
If Negative PC ← MM
MM
0000 0001 000
xxxxx
PC ← MM
MM
Unconditional
Branch
Conditional
Branches
Convenient Shorthand
If Zero PC ← 7
Notes: The K&S contains three instructions that will can change the Program Counter (PC).
- These are called the branching instructions.
There is one for the Negative flag
- if the negative flag is set (i.e. the last ALU result was negative in two’s complement)
- then change the PC to the address of the instruction we want to branch to.
- But if the negative flag is not set (i.e. the last ALU result was zero or positive in two’s complement)
- Then just go onto the next instruction.
There is one for the zero flag
- if the zero flag is set (i.e. the last ALU result was zero)
- then change the PC to the address of the instruction we want to branch to.
- But if the zero flag is not set (i.e. the last ALU result was any value but zero)
- Then just go onto the next instruction.
There is also an unconditional branch
- It changes the PC to the address of the instruction we want to branch to.
- There is no if, because there is no condition.
- The flags do not matter.
- E.g. when we reach the end of a while loop we need to branch to the top.
Like our other ML instructions we have a convenient shorthand that we can use to write programs:
- If Zero PC <- 7
- means if the last ALU result was zero (i.e. the zero flag is set)
- then put the address 7 (00111) into the PC.
- Then the next instruction that will run will come from address 7.
There are shorthands for the negative branch and the unconditional branch as well.

## Slide 11: K&S Machine Language Reference
Notes: Don’t discuss… just show it….
Maybe mention NOP,
- Once upon a time used as a timing device
- Run 1000 NOP and then do something.
- If they take 1/100 of a second each then we have waited 1 second.
- Much less useful as computers became more powerful and started running multiple programs simultaneously.
- I also has a use that we’ll see a little later
- when we discuss instruction cycle pipelining and “bubbles”

## Slide 12: Example
Machine Language Instruction
Operation
MM
0:
1:
2:
3:
4:
if R0 == R1
MM[20] ← R0
Done
Implement this program in K&S Machine Language.
Notes: Assume that there are values in R0 and R1.
- In a larger program the would have been put there by code.
- Just keeping it simple here.
Note that there is no instruction that will let us branch when two registers are equal…
- We only have instructions for zero or negative or unconditional.
- So you have to be a little creative!
For now
- Just write the operations out using our shorthand.
- If you finish that quickly
- then do the translation to ML.
See what they come up with.
- cover it.
- next slide contains a solution.
- may be similar, may be different.

## Slide 13: Example
Machine Language Instruction
Operation
R2 ← R0 - R1
if Zero PC ← 3
PC ← 4
MM[20] ← R0
HALT
MM
0:
1:
2:
3:
4:
if R0 == R1
MM[20] ← R0
Done
Implement this program in K&S Machine Language.
Pro Tip: You must do an ALU operation immediately before a conditional branch!
Notes: The appraoch here is to Subtract R1 from R0
- NOTE: R0-R1 will be zero if R0=R1
- So we’ll do R0 – R1
- If that gives a zero result the zero flag will be set
- So we can use the If Zero instruction to branch.
Here we will branch to 3
- At 3 we’ll put R0 into MM[20].
- Then the PC is incremented
- And we HALT at 4.
But what happens if R0 != R1?
- then the if Zero PC <- 3 branch will not be taken.
- When that happened the PC is incrementeed
- the next instruction is executed
- that is the unconditional branch PC <- 4
- Which jumps to the HALt
Can just look up the equivalent ML on the reference sheet.
- here the branch at 5 is a branch zero, to 7
- Can see the unsigned value 7 in the operand.
Note at end:
We have to construct all other branches using the 3 we have.
- turns out that’s enough to do everything we need to do.
- we’ll get some more experience with this in the activities and in later classes.

## Slide 14: Example
Machine Language Instruction
1010 0010 00 10 00 01
0000 0010 000 00011
0000 0001 000 00100
1000 0010 0 00 10100
1111 1111 1111 1111
Operation
R2 ← R0 - R1
if Zero PC ← 3
PC ← 4
MM[20] ← R0
HALT
MM
0:
1:
2:
3:
4:
if R0 == R1
MM[20] ← R0
Done
Implement this program in K&S Machine Language.
Notes: To translate, just look up the equivalent ML on the reference sheet.
The branch at 1 is a branch zero, to 3
- Can clearly see the unsigned value 3 in the operand.
The branch at 2 is an unconditional branch to 4
- Can clearly see the unsigned value 4 in the operand.

## Slide 15: Stored Program Computer
In a stored program computer, the program instructions and the data are stored in the main memory.
Program
Instructions
Data
Notes: We did something last time that I want to talk more about
It may not have seemed like a big deal…
- but this “trick” is the foundation of modern computing!
We put both the program instructions and the data on which they operate into the memory.
- This is what happens when you run a program …
- The instructions and data for the program are moved from the disk drive in your computer to the main memory.
- The Control Unit the causes those instructions to be executed:
- The PC indicates the instruction to be executed
- That instruction is moved from the memory to the IR
- The Instruction interpretation unit translates the ML instruction into micro-instructions
- The micro instructions configure the machine to carry out the operation.
Today, I want to first, put some conceptual structure on this “big idea”.
We’ll connect the K&S into the vocabulary and structures that are used to talk about modern computer architectures.
Then we’ll learn a little more about some additional capabilities of the K&S machine language.

## Slide 16: The “First” Stored Program Computer
Manchester Mark I – 1949
Frederic C. Williams, Tom Kilburn
Manchester, UK
EDVAC – 1949
John Mauchly, J. Presper Eckert
John Von Neuman, University of PA
Image from: https://en.wikipedia.org/wiki/
Manchester_Mark_1
Image from: https://en.wikipedia.org/wiki/EDSAC
Image from: https://www.thocp.net/
hardware/edvac.htm
EDSAC – 1949
Maurice Wilkes
Cambridge UK
Von Neuman
Architecture
Notes: The big idea here is that the program and the data are stored in the memory
Contrast with earlier computers we’ve seen where they had to be reconfigured for new programs.
This made these machines “General Purpose” computers.
- The same machine could do different computations
- Simply by loading it with a new program
- It did not require any reconfiguration.
Stored program computer sometimes also called the Von Neuman Architecture
Controversial term… idea originated with Mauchly and Eckert
Von Neuman
- very famous mathematician at the time came in to help refine idea
- he wrote a draft description that got out with just his name on it.
- It stuck.
You’ve gotten the idea that ”First” is somewhat controversial.
- Depends on exact definitions and timing particularly when things have been kept secret
- Really good history and interesting stories.
- Arguments can be made for any of these machines as the “first”
- Some really good books have been written about it,
- check them out if this type of history interests you.
===
EDSAC - Electronic Delay Storage Automatic Calculator
EDVAC, Electronic Discrete Variable Automatic Computer
- Origins of the idea in 1945
- Others built on the inspiration from this idea
- But it also didn’t run until 1949

## Slide 17: The Stored Program Architecture
Disk Drive (SSD/HDD),
Mouse, Monitor
Wifi, Network
Keyboard, Speakers,
…
Notes: Three main components:
- CPU – Central Processing Unit
- Where the computations are performed.
- Main Memory – or RAM
- Where the program instructions and data are stored.
- Input / Output
- Devices connected to the computer
- For moving information into and out of the CPU and memory
- All of your devices
- Disk drive, thumb drive
- network/wifi, bluettooth interface
- Mouse, keyboard
- speakers, monitors
The K&S very clearly has a CPU and main memory
It does not not support external I/O devices directly.

## Slide 18: The Central Processing Unit (CPU)
The CPU is made up of three interconnected components that control the machine and perform computations:
  The Arithmetic and Logic Unit (ALU)
  The General Purpose Registers
  The Control Unit (CU)
Notes: These are the same components that you have seen in operation in the K&S CPU
ALU
- Performs arithmetic and logical operations
- The K&S could do addition, or, and and subtraction.
- The ALU’s in modern processors can do hundreds of different operations.
- e.g. multiply / divide for signed, unsigned and floating point values.
Registers:
- Temporary storage for the data that is being used in the computations performed by the ALU.
Control Unit:
- Coordinates the instruction cycle by controlling the operation of all of the other components.

## Slide 19: The Instruction Cycle
The control unit coordinates the instruction cycle consisting of the three phases:
  Fetch, Decode and Execute.
Notes: Describe Fetch/Decode/Execute in general terms.
Fetch:
- The process of retrieving the next instruction from the main memory.
- The program counter (PC) gives the address of the next instruction
- The machine language (ML) instruction is moved from MM[PC] into the instruction register [IR]
Decode:
- The process of figuring out what the instruction in the IR is and how to configure the machine to carry it out.
- The instruction interpretation circuit uses the bits of the IR to compute the microinstruction needed.
- It is possible that complex operations may require multiple micro-instructions to complete.
Execute:
- The process by which the configured machine performs the operation indicated by the ML instruction that is in the IR
- Data moves around the machine, the ALU performs its operation, etc…
This is exactly what we have seen happening in the K&S
We really are just putting names to things we have seen before.

## Slide 20: The Instruction Cycle
Fetch
  IR ← MM[PC]
Decode
Execute
MM[2]: if negative branch to 4
Notes: Let’s trace through the instruction cycle in the K&S
- In class it would be just as well to do this via a live demo of the K&S
- Set it up to run the Example from earlier.
- Set R0, R1 not equal so we don’t take the first branch.
- Then take the second branch.
For this sequence of slides:
- Note that the PC = 2
- so we will be looking at the exeuction of the instruction at MM[2]
- That instruction happens to be If Negative PC <– 4
We know that the machine will Fetch/Decode/Execute
- over and over and over again.
Fetch
- Use the PC to find the instruction in memory.
- Move the ML instruction from MM[PC] to IR
- PC = 00010 = 2 (base 10)

## Slide 21: The Instruction Cycle
Fetch
  IR ← MM[PC]
Decode
  00000011000 00100
  if negative branch to 4
Execute
MM[2]: if negative branch to 4
Notes: The next thing that happens is decode…
The instruction interpretation unit uses the bits of the ML instruction in the IR to determine how to configure the machine.

## Slide 22: The Instruction Cycle
Fetch
  IR ← MM[PC]
Decode
  00000011000 00100
  if negative branch to 4
Execute
  Last ALU result negative?
  PC ← 4
MM[2]: if negative branch to 4
Notes: Once the instruction interpretation unit configures the machine via the microinstruction
The instruction is executed.
Check if the last ALU result was negative…
- Looking at the ALU, we can see that it was.
- So the instruction interpretation unit will set the PC to 4.
That means that the next fetch will be from 4
- we will skip over the instruction at 3.
Note that if the prior result was not Negative then
- We just do what we normally do
- PC = PC + 1.
- And we would have gone onto the instruction at 3 instead.

## Slide 23: The Instruction Cycle
Fetch
  IR ← MM[PC]
Decode
  00000011000 00100
  if negative branch to 4
Execute
  Last ALU result negative? PC ← 4
Fetch… Decode… Execute
MM[2]: if negative branch to 4
Notes: So now when we continue to fetch / decode / execute
The PC now contains 4
- So the next instruction is fetched from address 4
- instead of from address 3.

## Slide 24: Stored Program Architecture Summary
ML program instructions and data are stored in the main memory.
Stored Program Architecture
  CPU + Main Memory + Input/Output Devices
Instruction Cycle
  Fetch / Decode / Execute
    Program Counter (PC)
    Instruction Register (IR)
Central Processing Unit
  ALU + Registers + Control Unit
Notes: Nothing to talk about here.
Just a summary slide to bring it all together
Give them a chance to ask questions.

## Slide 25: Acknowledgments
https://creativecommons.org/licenses/by/4.0/
Slide Template From:
Slide Content Licensed as:
Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.
Notes: Note: Individual images may be covered by their own licensing agreements and were incorporated here under fair use. Their use in this slide deck does not change or alter their licensing.

## Slide 26: Motivating Branching
Programs often make decisions…
if (x < y) {
<code1>
}
else {
<code2>
}
while (i >= 0) {
<code>
}
for (i=0; i<10; i++) {
<code>
}
Notes: Branching code allows programs to make decisions
- To execute in one way under one condition
- And another way under a different codition
if
- if x < y then do instructions in code1 and skip code2
- Otherwise, skip code 1 and do instructions in code 2.
while
- repeat code as long as i>=0
- if I becomes less than 0 then skip over code and continue
for
- you get the idea…

## Slide 27: K&S Branching Machine Language Instructions
0000 0010 000
xxxxx
If Zero PC ← MM
MM
Branching Instructions
0000 0011 000
xxxxx
If Negative PC ← MM
MM
0000 0001 000
xxxxx
PC ← MM
MM
while (i >= 0) {
<code>
}
Unconditional
Branch
Notes: The K&S contains just three branching instructions.
- The one we saw was based on the Negative Flag.
There is one for the zero flag
- if the zero flag is set, then branch to the address given.
There is an unconditional branch
- Just change the PC so that we branch to a new instruction.
- E.g. when we reach the end of a while loop we need to branch to the top.

## Slide 28
CPU
Input/ Output
Main
Memory
(RAM)

## Slide 29
Input/ Output
Main
Memory
(RAM)

## Slide 30
General Purpose Registers
ALU
Control Unit
CPU