## Slide 1: 16 – Branching and Looping
COMP 256 – Dickinson College
Prof. Braught
Spring 2022
Image from: http://w34.co/no-arrays-javascript/

## Slide 2: Our Assembly Language So Far
Machine:
  16 Registers
    R0-R11 general purpose
  32-bit word size
  Memory Mapped I/O
Data Allocation
  Type directives
    .word
Instructions:
  Data Movement
    LOAD / STORE
  Arithmetic
    ADD / SUB / SHL / etc…
Addressing Modes:
  Register to Register
    ADD R3 R1 R4
  Direct Addressing Mode
    LOAD R2 X
  Immediate Addressing Mode
    SUB R3 R7 #1
Notes: This is just a recap of the relevant facts from the previous class.
- If anything doesn’t look familiar it would be worth reviewing #15.

## Slide 3: Motivating Branches
Compute the absolute value of x:
…
if (x < 0) {
x = -x;
}
…
Notes: If x is negative make it positive.
Otherwise do nothing.
In HLL we would just write the simple if statement.
In the machine language we will need a branch instruction.
- Something that changes the PC so that we skip over the x = -x if the value is not negative.
So, we need assembly language instructions that translate into the branching instructions we saw in ML.

## Slide 4: A Branching Example
Labels are used to identify the address (i.e. the target) for a branch.
e.g. XLTZ / XPOS
* Assembly Language
X: .word 0
LOAD R0 STDIN
STORE R0 X
BNEG R0 XLTZ * X < 0?
JUMP XPOS
* MM[X]  -MM[X]
XLTZ: NOT R0 R0 * X  ~X
ADD R0 R0 #1 * X  X + 1
STORE R0 X
XPOS: STORE R0 STDOUT
HALT
//HLL
int x;
Read x
if (x < 0) {
x = -x;
}
Print x
Notes: We read X from STDIN – from the keyboard
Put it into the address X
Then we implement the logic for the If statement
- If x is negative we branch to the body of the loop.
- Otherwise we jump over the body to the end of the loop.
Notice:
- In ASM we can just specify the register to check.
- Unlike ML where we had to do some operation in the ALU to set the flags
- Turns out the assembler takes care of that for us when it creates the machine language.
- It will generate ML instructions that do the following…
- R1 - R0
- If Negative PC <- SKIPIF
- If Zero PC <- SKIPIF
- So one ASM instruction may turn into multiple ML instructions.
- But we don’t have to care about it.
- That is a detail that is hidden from up by the Assembly Language Abstract Machine.
The body of the loop takes advantage of two’s complement representation to find –X
- It flips the bits with NOT
- Then it adds 1 using an Immediate Addressing Mode instruction.

## Slide 5: Generalized if Statement Structure
//HLL
…
if (condition) {
… if body …
}
…
* Assembly Language
…
Branch to IFBODY if condition is TRUE
JUMP to ENDIF
IFBODY: … ASM for if body …
ENDIF: …
Notes: We can give a general structure that can be used to implement any if statement.
There is nothing special about the IFBODY or ENDIF labels…
- in fact you could only use them once!
- So if you have multiple if statements you’ll need to use different labels.
- usually it is better to use meaningful names as we did in the prior example.
Note: There are lots of other ways to implement an if statement
- This is just a good template to use
- When you encounter any if statement you can do it this way.

## Slide 6: All the Branching Instructions
Notes: BNEG example of checking a single register.
- BPOS, BZERO, BNZERO, BODD, BEVEN
BLEQ two registers – comparison
- BEQ, BNEQ, BGT, BGEQ, BLT
- A BLT might be BLEQ if you don’t like tomatoes or bacon ;)
JUMP unconditional branch.

## Slide 7
//HLL
int x;
int y;
Read x
Read y
if (x >= y) {
y = x + 5
}
Print y
Challenge
Translate this HLL program into assembly language.
Assemble and run it on the machine simulator.

## Slide 8
//HLL
int x;
int y;
Read x
Read y
if (x >= y) {
y = x + 5
}
Print y
Challenge
* Assembly Language
X: .word 0
Y: .word 0
LOAD R0 STDIN
STORE R0 X
LOAD R1 STDIN
STORE R1 Y
BGEQ R0 R1 SETY * X >= Y
JUMP PRINTY
SETY: ADD R1 R0 #5 * Y  X + 5
STORE R1 Y
PRINTY: STORE R1 STDOUT
HALT

## Slide 9: for Loop Example
Compute the sum of the numbers from 1 up to and including n.
Initialization
Condition
Update
Loop
Body
//HLL
int n;
int sum=0;
Read n
for (i=1; i<=n; i++) {
sum = sum + i;
}
Print sum
Notes: Let’s look at an example of a for loop.
Recall for loop parts…
- initialization... Once before loop
- condition… each time before loop
- if condition is true the loop body is executed
- if condition is false the loop body is skipped.
- update… at end of each loop

## Slide 10: Generalized for Loop Structure
Loop conditions are often checked at the bottom of the loop in assembly language.
//HLL
…
for (init; condition; update) {
… loop body …
}
…
* Assembly Language
…
… init …
JUMP COND
TOP: … loop body …
… update …
COND: Branch to TOP if condition is TRUE.
…
Notes: Here is the general structure for a for loop.
- Anytime you see a for loop in your code you can do this…
Typically, what is done with loops is to move the condition to the bottom of the loop.
- We check if the loop condition is true
- If it is then we jump back to the top and do the loop body.
- At the end of the loop body we do the update
- Then we check the condition again.
Again, it may seem a little odd to do it that way
- But ultimately it just make the code a little simpler.
- It also happens to reduces control hazards in the instruction pipeline
- as compared to implementing it in a more straight forward way.

## Slide 11: for Loop Example
int n;
int sum=0;
Read n
for (i=1; i<=n; i++) {
sum = sum + i;
}
Print sum
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R1 #1 * R1 is i
LOAD R2 SUM * R2 is temporary sum
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT

## Slide 12: Tracing the for Loop Example
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R1 #1 * R1 is i
LOAD R2 SUM * R2 is temporary sum
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT
Registers
R0: ?
R1: ?
R2: ?
STDIN:
STDOUT:
5
Console
Main Memory
0:
4:
…:
92:
96:
N 100: ?
SUM 104: 0
…:
ML
Program Instructions
(N)
(i)
(SUM)

## Slide 13: Tracing the for Loop Example
Registers
R0: 5
R1: ?
R2: ?
STDIN:
STDOUT:
5
Console
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 0
…:
ML
Program Instructions
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R1 #1 * R1 is i
LOAD R2 SUM * R2 is temporary sum
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT
(N)
(i)
(SUM)
Notes: Read the 5 from STDIN
Place it into R0
And then into MM[X]

## Slide 14: Tracing the for Loop Example
Registers
R0: 5
R1: 1
R2: 0
STDIN:
STDOUT:
Console
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 0
…:
ML
Program Instructions
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R1 #1 * R1 is i
LOAD R2 SUM * R2 is temporary sum
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT
(N)
(i)
(SUM)
Notes: Load R1 with the value 1 to initialize i
Use R2 as sum so we don’t have to load it from memory every time.

## Slide 15: Tracing the for Loop Example
Registers
R0: 5
R1: 1
R2: 0
STDIN:
STDOUT:
Console
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 0
…:
ML
Program Instructions
(N)
(i)
(SUM)
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R1 #1 * R1 is i
LOAD R2 SUM * R2 is temporary sum
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT
Notes: Jump to the condition
Check R1 <= R0?
- True 1 <= 5
- Branch back to top!

## Slide 16: Tracing the for Loop Example
Registers
R0: 5
R1: 1
R2: 0
STDIN:
STDOUT:
Console
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 0
…:
ML
Program Instructions
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R1 #1 * R1 is i
LOAD R2 SUM * R2 is temporary sum
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT
(N)
(i)
(SUM)

## Slide 17: Tracing the for Loop Example
Registers
R0: 5
R1: 1
R2: 1
STDIN:
STDOUT:
Console
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 0
…:
ML
Program Instructions
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R1 #1 * R1 is i
LOAD R2 SUM * R2 is temporary sum
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT
(N)
(i)
(SUM)

## Slide 18: Tracing the for Loop Example
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R1 #1 * R1 is i
LOAD R2 SUM * R2 is temporary sum
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT
Registers
R0: 5
R1: 1
R2: 1
STDIN:
STDOUT:
Console
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 0
…:
ML
Program Instructions
(N)
(i)
(SUM)

## Slide 19: Tracing the for Loop Example
Registers
R0: 5
R1: 2
R2: 1
STDIN:
STDOUT:
Console
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 0
…:
ML
Program Instructions
(N)
(i)
(SUM)
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R1 #1 * R1 is i
LOAD R2 SUM * R2 is temporary sum
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT

## Slide 20: Tracing the for Loop Example
Registers
R0: 5
R1: 2
R2: 1
STDIN:
STDOUT:
Console
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 0
…:
ML
Program Instructions
(N)
(i)
(SUM)
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R1 #1 * R1 is i
LOAD R2 SUM * R2 is temporary sum
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT
Notes: Check condition again…
- R1 <= R0
- 2 <= 5 - True
- back to to the top

## Slide 21: Tracing the for Loop Example
Registers
R0: 5
R1: 2
R2: 1
STDIN:
STDOUT:
Console
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 0
…:
ML
Program Instructions
(N)
(i)
(SUM)
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R1 #1 * R1 is i
LOAD R2 SUM * R2 is temporary sum
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT

## Slide 22: Tracing the for Loop Example
Registers
R0: 5
R1: 3
R2: 3
STDIN:
STDOUT:
Console
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 0
…:
ML
Program Instructions
(N)
(i)
(SUM)
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R1 #1 * R1 is i
LOAD R2 SUM * R2 is temporary sum
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT

## Slide 23: Tracing the for Loop Example
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R1 #1 * R1 is i
LOAD R2 SUM * R2 is temporary sum
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT
Registers
R0: 5
R1: 3
R2: 3
STDIN:
STDOUT:
Console
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 0
…:
ML
Program Instructions
(N)
(i)
(SUM)
Notes: 3 <= 5
- True
- Back to top
- Do it again
- Make
- R2 3 + 3 = 6
- R1 3 + 1 = 4

## Slide 24: Tracing the for Loop Example
Registers
R0: 5
R1: 4
R2: 6
STDIN:
STDOUT:
Console
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 0
…:
ML
Program Instructions
(N)
(i)
(SUM)
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R1 #1 * R1 is i
LOAD R2 SUM * R2 is temporary sum
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT
Notes: 4 <= 5
- True
- Back to top and do it again
- Make
- R2 = 6 + 4 = 10
- R1 = 4 + 1 = 5

## Slide 25: Tracing the for Loop Example
Registers
R0: 5
R1: 5
R2: 10
STDIN:
STDOUT:
Console
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 0
…:
ML
Program Instructions
(N)
(i)
(SUM)
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R1 #1 * R1 is i
LOAD R2 SUM * R2 is temporary sum
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT
Notes: 5 <= 5
- True
- Back to top and do it again
- Make
- R2 = 10 + 5 = 15
- R1 = 5 + 1 = 6

## Slide 26: Tracing the for Loop Example
Registers
R0: 5
R1: 6
R2: 15
STDIN:
STDOUT:
Console
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 0
…:
ML
Program Instructions
(N)
(i)
(SUM)
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R1 #1 * R1 is i
LOAD R2 SUM * R2 is temporary sum
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT
Notes: 6 <= 5
- False….
- Don’t go to top… just continue

## Slide 27: Tracing the for Loop Example
Registers
R0: 5
R1: 6
R2: 15
STDIN:
STDOUT:
Console
15
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 15
…:
ML
Program Instructions
(N)
(i)
(SUM)
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R1 #1 * R1 is i
LOAD R2 SUM * R2 is temporary sum
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT
Notes: Put R2 into MM[SUM]
Display R2

## Slide 28: Acknowledgments
https://creativecommons.org/licenses/by/4.0/
Slide Template From:
Slide Content Licensed as:
Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.
Notes: Note: Individual images may be covered by their own licensing agreements and were incorporated here under fair use. Their use in this slide deck does not change or alter their licensing.

## Slide 29: The General the if Structure
Notes: This is the resource you’ll use in the activities.
It shows
- the HLL construct at the top (C)
- And the ASM structure at the bottom.
Very much the same as what we just saw.
- But it gives a template that can be used to build any of the different HLL structures.