## Slide 1: 02 – Transistors to Logic Gates
COMP 256 – Dickinson College
Prof. Braught
Spring 2022
Notes: Before we start…
- Questions on Syllabus?
- Grading clear enough for now?
- We’ll discuss more as things come in and get returned.
- Open to questions at any time.

## Slide 2: The Hardware Abstraction Hierarchy
The Hardware abstraction hierarchy bridges the gap from electrical signals to programmable machines that perform useful computation.
  Electrical signals
  0’s and 1’s
  Transistors
  Logic gates
  Circuits
  Programmable machines
Image from: https://www.aroundkent.net/
computational-thinking-a-world-of-1s-and-0s
Photo by: Steven Gerner, https://www.flickr.com/photos/
sgerner/16477700444/in/photostream/
Notes: Electrical Signals: Voltages and currents
0’s and 1’s: Define conventions for interpreting the electrical signals as abstract 0’s and 1’s
Transistors: Use those 0’s and 1’s as abstractions to control transistors
Logic Gates: Combine transistors into circuits and treat them as logic gates
Circuits: Combine logic gates into more complex circuits that perform specific functions.
Combine those into machines that do useful computation
At each level, we are able to hide and forget about the details of the lower levels (mostly).

## Slide 3: Voltages and 0’s and 1’s … oh my! *
1
0
Image from: https://openclipart.org/
Voltages are the physical representation of the 0’s and 1’s that we think of being manipulated by computers.
  Low voltages close to 0V (Volts), also called ground, represent 0.
  Positive voltages, close to some maximum (e.g. 1.8V, 3.3V or 5V), represent 1.
    Different applications use different voltage levels to represent 1 depending upon noise and power consumption constraints.
* Cultural Reference: The Wizard of Oz.
Notes: One way to think of this is as a battery:
- if a voltage is the same as the + side of the battery then it will be a 1
- if a voltage is the same as the – side of the battery then it will be a 0.
Need to be able to reliably differentiate between ground (0V)
And the voltage that is chosen to be (1)
In the presence of electronic noise (think radio static or phone call breakup).
Beyond the scope of this course.
- one of the details we will ignore in our abstractions

## Slide 4: A Metaphor: Voltage-Controlled Switches
Images from: http://www.learningaboutelectronics.com/Articles/Door-alarm-circuit.php
0
Open
1
Closed
Images from:
https://openclipart.org/
Images from:
https://openclipart.org/
OFF
ON
Notes: All computation in modern computers is based on voltage-controlled switches.
- We will see a number of different technologies that have been used to build voltage-controlled switches
- These roughly correspond to a chronological history of how computers have been constructed.
Regardless of the technology used to build them, this metaphor explains how they behave.
0 being ground – turns switch off or open – no current flows – an attached light will be off.
1 being positive voltage – turns switch on or closed – current flows – an attached light will be on.
When current flows or doesn’t flow,
- it can go on to create voltages that will open or close other switches.
- This cascading is ultimately what does the computation in the computer.
****** Note can also have switches that behave the other way around.
Closed when there is a 0, open when there is a 1.
We’ll see those soon.

## Slide 5: The First Switches
The first digital computers were built using Electromagnetic Relays.
  Electrically controlled switches.
Images from: https://www.gomog.com/BLAIR/
tech/electrical/relay/troubleshoot_relay.html
Spring
Notes: Think nail with wire wrapped around it in science class years ago!
Spring holds movable contact up
- the switch is open (off)
When electromagnet turns on, it pulls the movable contact down
- the switch is closed (on)
Fast but the mechanical movement does place limits on how fast.
Also have an issue of mechanical wear and tear
- turning on and off millions of times.
- Contacts or springs break.
Also very noisy!! Thousands of these clacking open and closed tens/hundreds of times per second.

## Slide 6: Faster Switches
Relays were later replaced with Vacuum Tubes.
  Electrically controlled switches
  No moving parts
  Faster and cheaper and more reliable!
Image from: http://www.quantumday.com/2012/07/
nanotechnology-and-vacuum-tube.html
Notes: No moving parts, so there can’t be an actual switch.
Strange…
How they work is beyond the scope of this course.
But idea is the same and as an abstraction we can think of them as a switch…
- Applying a 1 makes it behave like a closed switch letting current flow.
- Applying a 0 makes it behave like an open switch stopping current from flowing.
Look like lightbulbs.
Can burn out like lightbulbs
Generated reliability issues

## Slide 7: Transistors – Super Fast Switches
Modern computers are built using Transistors
  Electrically controlled switches.
  Solid state
  Revolutionary - Way smaller, way faster, way cheaper, way more reliable!
Image from: http://www.megaprocessor.com/
Image from: https://www.explainthatstuff.com/
integratedcircuits.html
Notes: Solid material, no moving parts, nothing to burn out.
Can run for decades!!
But again as an abstraction:
1 lets current flow – acts like closed switch
0 does not let current flow – acts like open switch
Left: Discrete or individual transistors
Right: Integrated circuit
- containing lots of transistors in a single package.
- organized as an abstraction…
- inputs go in, results of computations come out.
- e.g. input 0’s and 1’s representing numbers… out come 0’s and 1’s represnting their sum

## Slide 8: CMOS Transistors
Metal Oxide Semiconductor (MOS)
  Most common transistor technology in modern computer designs.
CMOS: Complementary MOS Transistors
  Two types that behave in complementary ways:
    NMOS transistors
    PMOS transistors
      N or P are types of impurities that are added to the silicon when a transistor is made in order to change its behavior.
Notes: Complementary ways – we’ll see what that means in a moment.

## Slide 9: N-Type or NMOS Transistors
NMOS Transistor
  3 connections
    (S)ource
    (G)ate
    (D)rain
  Gate value controls the switch.
    G = 0 - Switch is open
    G = 1 – Switch is closed
DGS
N
S
D
G
0
N
S
D
G
1
Image from: https://openclipart.org/
Notes: No actual switch… but useful way to think about them as an abstraction.
N-Type are indicated by
- the little (N)
- with the Drain on top
- with the Source on the bottom.
NOTE: DGS ordering of terminals is based on TINKERCAD.
This may need to be updated to match physical component when back in actual lab.

## Slide 10: An NMOS Transistor in Our Metaphor
0
1
Open
Closed
N
S
D
G
0
N
S
D
G
1
OFF
ON
Notes: So an NMOS transistor behaves just like the electrically controlled switch from our metaphor.

## Slide 11: P-Type or PMOS Transistors
PMOS Transistor
  3 connections
    (S)ource
    (G)ate
    (D)rain
  Gate value controls the switch.
    G = 0 - Switch is closed
    G = 1 – Switch is open
SGD
P
S
D
G
0
1
P
S
D
G
Notes: PMOS is the complement of NMOS
They look exactly the same
They have the same 3 contacts … sometimes reversed… but…
They behave in the opposite (complementary) way.
P-Type are indicated by
- the little (P)
- with the Drain on bottom
- with the Source on the top.
NOTE: SGD is based on TINKERCAD
It may need to be updated to match physical component when back in the lab.

## Slide 12: Quick Check
Use our abstraction of NMOS and PMOS transistors to indicate which switches would be open an which would be closed.
P
S
D
G
N
S
D
G
N
S
D
G
P
S
D
G
0
0
1
1
Notes: Think and then compare with your neighbors.
Come to consensus.
Any disagreements?

## Slide 13: A CMOS Circuit
CMOS Circuits are created by connecting multiple transistors together.
0’s (ground, -) and 1’s (power, +) are connected.
Connections at intersections will be indicated by a thick dot.
P
S
D
G
N
S
D
G
0
1
Input
Output
Notes: If wires cross without having a thick dot then there is no connection at that point.

## Slide 14: A CMOS Circuit
CMOS Circuits are created by connecting multiple transistors together.
0’s (ground, -) and 1’s (power, +) are connected.
A 0 or 1 is applied at the input.
The 0’s or 1’s flow from sources to drains setting the output.
1
0
1
Input
Output
0
P
S
D
G
N
S
D
G
P
S
D
G
N
S
D
G
0
1
Input
Output
Notes: Can think about gate as faucet as well.
Then think about 0 or 1 at source flowing like water.

## Slide 15: A CMOS Circuit
P
S
D
G
N
S
D
G
0
1
Input
Output
CMOS Circuits are created by connecting multiple transistors together.
0’s (ground, -) and 1’s (power, +) are connected.
A 0 or 1 is applied at the input.
The 0’s or 1’s flow from sources to drains setting the output.
What will the output of this CMOS circuit be if the input is 1? Why?
1
Notes: The other possibility for the input is a 1.
Think it through.
Compare with a neighbor.
Come to consensus.
Discuss and draw it out.

## Slide 16: CMOS Circuit Rule
The 0’s or 1’s flow from sources to drains setting the output.
  In a correct circuit there will:
    always be at least one path from a 1 or a 0 to the output.
    never be a path from both a 1 and a 0 to the output.
Notes: - Physics 213 if you are interested in learning more about transistors.

## Slide 17
Thinking about a bunch of transistors and their “switches” and whether they are open or closed can be difficult.
If only there were some way to just think about what the circuit computes and forget about the specific configuration and operation of the transistors.
🤔
Notes: You’ll see that in the homework.

## Slide 18: Challenge:
What are all of the possible combinations of 0’s and 1’s that can be used as inputs A and B to this CMOS circuit?
What output (Z) is produced for each of those possible input combinations?
Notes: Notice, that the wire from b to the right hand NMOS transistor crosses another wire without a connection (no thick dot).

## Slide 19: What’s Next?
HW 02 – Due Friday 8:30am
  Submit to Moodle
Lab 01 – Tomorrow 3:00
  Tome 231

## Slide 20: Acknowledgments
https://creativecommons.org/licenses/by/4.0/
Slide Template From:
Slide Content Licensed as:
Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.

## Slide 21: A Metaphor: Voltage-Controlled Switches
0
1
Open
Closed
Images from:
https://openclipart.org/
Images from:
https://openclipart.org/
Images from: http://www.learningaboutelectronics.com/Articles/Door-alarm-circuit.php
OFF
ON
Notes: All computation in modern computers is based on voltage-controlled switches.
- We will see a number of different technologies that have been used to build voltage-controlled switches
- These roughly correspond to a chronological history of how computers have been constructed.
Regardless of the technology used to build them, this metaphor explains how they behave.
0 being ground – turns switch off or open – no current flows – an attached light will be off.
1 being positive voltage – turns switch on or closed – current flows – an attached light will be on.
When current flows or doesn’t flow,
- it can go on to create voltages that will open or close other switches.
- This cascading is ultimately what does the computation in the computer.
****** Note can also have switches that behave the other way around.
Closed when there is a 0, open when there is a 1.
We’ll see those soon.

## Slide 22
P
S
D
G
N
S
D
G
N
S
D
G
0
N
S
D
G
1
0
1
P
S
D
G
P
S
D
G

## Slide 23
P
S
D
G
N
S
D
G
0
1
P
S
D
G
N
S
D
G
1
Z
A
B
Notes: NAND

## Slide 24
P
S
D
G
N
S
D
G
0
P
S
D
G
N
S
D
G
1
Z
A
B
0
Notes: NOR

## Slide 25
By inductiveload - Own work using: Inkscape 0.43, Public Domain, https://commons.wikimedia.org/w/index.php?curid=943028
1
1
0
0
0

## Slide 26: A CMOS Circuit
0
1
Input
Output
P
S
D
G
N
S
D
G
P
S
D
G
N
S
D
G
0
1
Input
Output
Circuits are created by connecting multiple transistors together.
0’s (ground, -) and 1’s (power, +) are connected.
A 0 or 1 is applied at the input.
The 0’s or 1’s flow from sources to drains setting the output.
0
1
Notes: In this case the switches are reversed
- P open
- N closed

## Slide 27: CMOS Circuit Rules
PMOS Source is always closer to 1 than to 0.
  i.e. power or + battery terminal
NMOS Source is always closer to 0 than to 1.
  i.e to ground or – battery terminal
The path through the transistors (switches) to either 0 or 1 determines the output.
  In a correct circuit there will:
    always be at least one path to 1 or to 0.
    never be a path to both 1 and 0.
Notes: Rules of thumb when designing circuits using CMOS.
These are required for our abstraction of transistors as switches works…
If the transistors just like switches then these rules (at least the first two) wouldn’t matter.
But if we don’t use them in this way, then the details we are ignoring will cause the abstraction to fail.
So sort of like the while loop program you saw…
- when we use an abstraction outside of its intended scope it fails.
- we then need to know the details to understand why it does what it does.
We will understand that program… but not the transistor…
- Physics 213 if you are interested.