## Slide 1: LA3 – Branching and Looping
COMP 256 – Dickinson College
Prof. Braught
Spring 2023
Image from: http://w34.co/no-arrays-javascript/

## Slide 2: Our Assembly Language So Far
Machine:
  16 Registers
    R0-R11 general purpose
    R12-15 reserved
  32-bit word size
  Memory Mapped I/O
Data Allocation
  Type directives
    .word
Instructions:
  Data Movement
    LOAD / STORE
  Arithmetic
    ADD / SUB / SHL / etc…
Addressing Modes:
  Register to Register
    ADD R3 R1 R4
  Direct Addressing Mode
    LOAD R2 X
  Immediate Addressing Mode
    SUB R3 R7 #1
Notes: This is just a recap of the relevant facts from the previous class.
- If anything doesn’t look familiar it would be worth reviewing LA2.

## Slide 3: Motivating Branches
Compute the absolute value of x:
…
if (x < 0) {
x = -x;
}
…
Notes: If x is negative make it positive.
Otherwise do nothing.
In HLL we would just write the simple if statement.
In the machine language we saw that we can use a branching instruction or a combination of branching instructions.
- Recall that the branching instructions either
- Allowed the PC to increment so that the next instruction in memory was fetched (if the condition did not hold)
- E.g. here if x >= 0 we skip the x=-x statement
- Also recall that we often inverted the conditions.
- Or changed the PC so that we jumped to a specified address to fetch the next instruction (if the condition held)
- E.g. here we would skip over the x = -x if the value is not negative.
So, we need assembly language instructions that do the same kind of thing.

## Slide 4: A Branching Example
Labels are used to identify the address (i.e. the target) for a branch.
e.g. XLTZ / XPOS
* Assembly Language
X: .word 0
LOAD R0 STDIN
STORE R0 X
BNEG R0 XLTZ * X < 0?
JUMP XPOS
* MM[X]  -MM[X]
XLTZ: NOT R0 R0 * X  ~X
ADD R0 R0 #1 * X  X + 1
STORE R0 X
XPOS: STORE R0 STDOUT
HALT
//HLL
int x;
Read x
if (x < 0) {
x = -x;
}
Print x
Notes: This is the HLL Program from the last slide that
- reads a value
- computes its absolute value
- prints the result
- Note that the strange spacing will just help align the HLL with the assembly language translation.
We read X from STDIN – from the keyboard
Put it into the address X
Then we implement the logic for the If statement
- If x is negative we branch to the body of the if statement (XLTZ – an acronym for X less than Zero)
- We then continue with the statement labeled XPOS, because it is just the next statement (PC = PC + 1)
- That prints out the absolute value and stops.
- Otherwise we jump over the body to the end of the loop. (XPOS - short for X is positive)
- We just print the number X itself because it was already positive.
Notice:
- In ASM if we want to check if a register is negative we can just specify the register
- Unlike in ML where we had to do some ALU operation to set the ALU flags used by the branching instruction.
- In Assembly, we don’t have to worry about hat.
- The assembler takes care of it for us when it creates the machine language.
- It will generate ML instructions that do the following…
- R0 | R0 to set the ALU flags.
- If Negative PC <- XLTZ
- Otherwise PC <- XPOS
- So one ASM instruction may turn into multiple ML instructions.
- But we don’t have to care about it.
- That is a detail that is hidden from up by the Assembly Language Abstract Machine.
The body of the loop takes advantage of two’s complement representation to find -X
- It flips the bits with NOT
- Then it adds 1 using an Immediate Addressing Mode instruction.
- Puts the result into X
- Then we continue on to the next instruction
- Print the result
- Stop.

## Slide 5: Generalized if Statement Structure
//HLL
…
if (condition) {
… if body …
}
…
* Assembly Language
…
Branch to IFBODY if condition is TRUE
JUMP to ENDIF
IFBODY: … ASM for if body …
ENDIF: …
Notes: We can generalize that structure so that it can be used to implement any if statement.
Note: There is nothing special about the IFBODY or ENDIF labels…
- They are just place holders here for labels that you will choose that makes more sense.
- You need to customize the labels in your program
- They must be unique, a label may only be used once in a program.
- like we did with XLTZ and XPOS in the prior example.
- Use meaningful names so that your program is easier to read.
Note: There are lots of other ways to implement an if statement
- This is just a fairly straight forward way to do it that will always work.
- Some of the other ways are a little more efficient if you want to puzzle them out.
- E.g. here you can implement the if statement with one less branching statement by inverting the condition.

## Slide 6: All the Branching Instructions
Notes: Here are all of the branching instructions in our assembly langauge.
- There are a lot of them.
- Having more ASM branches just makes it easier for us to write the programs
- Ultimately the assembler turns these all into an ALU operation followed by one or more ML branching instructions.
- E.g. branch on zero, negative or unconditionally
- like the ones worked out back in the homework on Machine language branching.
- A machine more sophisticated than the K&S may include more ML branches in its hardware as well.
BNEG is an example of checking a single register.
- BLOC (short for branch location) is just a place holder for a label.
- Replace it with the label you want to branch to.
- BPOS, BZERO, BNZERO, BODD, BEVEN
- Note again,
- the assembler converts each of these to an ALU operation in ML
- followed by the necessary ML branching instructions.
BLEQ is an example of comparing two registers.
- BEQ, BNEQ, BGT, BGEQ, BLT
- A BLT might be BLEQ if you don’t like tomatoes or bacon ;)
- Note again…. Get it by now… what does the assembler do?
JUMP is an unconditional branch.

## Slide 7
//HLL
int x;
int y;
Read x
Read y
if (x >= y) {
y = x + 5
}
Print y
Challenge 1
Translate this HLL program into assembly language.
Assemble and run it on the machine simulator.
Notes: Take about 10 minutes to try this.
Work in pairs if you like.
Use the template on the earlier slide for how to construct an if statement.
If you finish this quickly, there is another challenge on the next slide.

## Slide 8
//HLL
int x;
int y;
Read x
Read y
if (x != y) {
x = y;
}
else {
x = y + 1
}
Print x
Challenge 2
If you finish the first one, try to translate this HLL program into assembly language.
Assemble and run it on the machine simulator.

## Slide 9
//HLL
int x;
int y;
Read x
Read y
if (x >= y) {
y = x + 5
}
Print y
Challenge 1
* Assembly Language
X: .word 0
Y: .word 0
LOAD R0 STDIN
STORE R0 X
LOAD R1 STDIN
STORE R1 Y
BGEQ R0 R1 SETY * X >= Y
JUMP PRINTY
SETY: ADD R1 R0 #5 * Y  X + 5
STORE R1 Y
PRINTY: STORE R1 STDOUT
HALT
Notes: This uses the generalized if statement template to convert the HLL code to ASM.
- Notice:
- The BGEQ translates the if condition and branches to the body of the loop at SETY
- At the end of the loop body the execution just continues to the next instruction
- The JUMP skips the body of the loop
- Prints the result
- Halts

## Slide 10: for Loop Example
Compute the sum of the numbers from 1 up to and including n.
Initialization
Condition
Update
Loop
Body
//HLL
int n;
int sum=0;
Read n
for (i=1; i<=n; i++) {
sum = sum + i;
}
Print sum
Notes: Let’s look at an example of a for loop.
This task is fairly straight forward with a for loop in a HLL.
Recall for loop parts…
- initialization... Once before loop
- condition… each time before loop
- if condition is true the loop body is executed
- if condition is false the loop body is skipped.
- update… at end of each loop
Our task here will be to translate those parts into an equivalent in Assembly Langauge.

## Slide 11: Generalized for Loop Structure
Pro Tip: Loop conditions are often checked at the bottom of a loop in assembly language.
//HLL
…
for (init; condition; update) {
… loop body …
… loop body …
… loop body …
}
…
* Assembly Language
…
… init …
JUMP COND
TOP: … loop body …
… loop body …
… loop body …
… update …
COND: Branch to TOP if condition is TRUE.
…
Notes: Here is the general structure for a for loop.
- Anytime you see a for loop in your code you can do this…
Typically, what is done with for loops is to move the condition and the update to the bottom of the loop.
- This just simplifies the code since the update done at the end of the loop.
- We check if the loop condition is true
- If it is then we jump back to the top and do the loop body.
- At the end of the loop body we do the update
- Then we check the condition again.
Again, it may seem a little odd to do it that way
- But ultimately it just make the code a little simpler.
- It also happens to reduces control hazards in the instruction pipeline
- as compared to implementing it in a more straight forward way.

## Slide 12: for Loop Example
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R2 SUM * R2 is temporary sum
LOAD R1 #1 * R1 is i
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT
int n;
int sum=0;
Read n
for (i=1; i<=n; i++) {
sum = sum + i;
}
Print sum
Notes: We do the normal stuff
- create labels
- read the result in
…init…
- LOAD R2 SUM
- not technically part of init
- but we will need SUM repeatedly through the loop
- so we’ll put it into a register here.
- Use R1 as i and set its initial value to 1.
…JUMP COND…
- Jump to the bottom of the loop
- There we check the condition of the loop
- Is R1 less than or equal to R0
- i.e. is i <= N
- If so, go to the top of the loop body
- otherwise the loop is done and just continue onto the next instruction
- save the result into SUM
- Print it.
- Stop
…loop body…
- If we BLEQ back to the TOP then we need to execute the loop body.
- Here that is
- ADD R2 R2 R1
- Which is SUM = SUM + 1
…update…
- After the loop body completes
- we would go up and do the update in the for statement
- in assembly we just place it as the next line right at the end of the loop body.
- ADD R1 R1 #1
- i = i + 1
Then we would check the condition again…
- if still BLEQ R1 R0 then back to the top to do it again…

## Slide 13: Tracing the for Loop Example
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R1 #1 * R1 is i
LOAD R2 SUM * R2 is temporary sum
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT
Registers
R0: ?
R1: ?
R2: ?
STDIN:
STDOUT:
5
Console
Main Memory
0:
4:
…:
92:
96:
N 100: ?
SUM 104: 0
…:
ML
Program Instructions
(N)
(i)
(SUM)
Notes: The Remainder of the slides walk through the execution of the for loop program in detail.
They show the contents of the memory and the registers.
- So you can see what is happening behind the abstraction.
If there is time we will trace through this in detail.
- If not there are highlights and explanatory comments on each slide
- You can trace through how it works yourself.

## Slide 14: Tracing the for Loop Example
Registers
R0: 5
R1: ?
R2: ?
STDIN:
STDOUT:
5
Console
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 0
…:
ML
Program Instructions
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R2 SUM * R2 is temporary sum
LOAD R1 #1 * R1 is i
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT
(N)
(i)
(SUM)
Notes: Read the 5 from STDIN
Place it into R0
And then into MM[N], i.e.. MM[100]
- recall that labels (like N) are a memory address.

## Slide 15: Tracing the for Loop Example
Registers
R0: 5
R1: 1
R2: 0
STDIN:
STDOUT:
Console
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 0
…:
ML
Program Instructions
(N)
(i)
(SUM)
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R2 SUM * R2 is temporary sum
LOAD R1 #1 * R1 is i
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT
Notes: …init…
Use R2 as sum so we don’t have to load it from memory every time.
- again, this is not technically part of the for loop init
- but SUM will be needed throughout the loop
- We could load and store it into memory each time we use it
- but it’s a lot faster and more efficient to just use a register.
Load R1 with the value 1 to initialize I
- This is the init.

## Slide 16: Tracing the for Loop Example
Registers
R0: 5
R1: 1
R2: 0
STDIN:
STDOUT:
Console
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 0
…:
ML
Program Instructions
(N)
(i)
(SUM)
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R2 SUM * R2 is temporary sum
LOAD R1 #1 * R1 is i
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT
Notes: Jump to the condition at the end of the loop.
Check R1 <= R0?
- True 1 <= 5
- Branch back to top!

## Slide 17: Tracing the for Loop Example
Registers
R0: 5
R1: 1
R2: 0
STDIN:
STDOUT:
Console
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 0
…:
ML
Program Instructions
(N)
(i)
(SUM)
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R2 SUM * R2 is temporary sum
LOAD R1 #1 * R1 is i
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT
Notes: …loop body…
- ADD R2 R2 1
- Sets R2 to its current value + 1 (because R1 = 1)
- So R2 will become 1
- next slide.

## Slide 18: Tracing the for Loop Example
Registers
R0: 5
R1: 1
R2: 1
STDIN:
STDOUT:
Console
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 0
…:
ML
Program Instructions
(N)
(i)
(SUM)
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R2 SUM * R2 is temporary sum
LOAD R1 #1 * R1 is i
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT
Notes: Here R2 has become 1.

## Slide 19: Tracing the for Loop Example
Registers
R0: 5
R1: 1
R2: 1
STDIN:
STDOUT:
Console
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 0
…:
ML
Program Instructions
(N)
(i)
(SUM)
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R2 SUM * R2 is temporary sum
LOAD R1 #1 * R1 is i
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT
Notes: …update…
- ADD R1 R1 #1
- i = i + 1
- i will become 2
- next slide.

## Slide 20: Tracing the for Loop Example
Registers
R0: 5
R1: 2
R2: 1
STDIN:
STDOUT:
Console
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 0
…:
ML
Program Instructions
(N)
(i)
(SUM)
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R2 SUM * R2 is temporary sum
LOAD R1 #1 * R1 is i
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT
Notes: Here, i has become 2

## Slide 21: Tracing the for Loop Example
Registers
R0: 5
R1: 2
R2: 1
STDIN:
STDOUT:
Console
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 0
…:
ML
Program Instructions
(N)
(i)
(SUM)
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R2 SUM * R2 is temporary sum
LOAD R1 #1 * R1 is i
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT
Notes: Check condition again…
- R1 <= R0
- 2 <= 5 - True
- back to to the top of the loop.

## Slide 22: Tracing the for Loop Example
Registers
R0: 5
R1: 2
R2: 1
STDIN:
STDOUT:
Console
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 0
…:
ML
Program Instructions
(N)
(i)
(SUM)
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R2 SUM * R2 is temporary sum
LOAD R1 #1 * R1 is i
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT
Notes: …loop body…
- ADD R2 R2 R1
- R2 will become 1 + 2 = 3.
…update…
- ADD R1 R1#1
- R1 will become 2 + 1 = 3
Next slide.

## Slide 23: Tracing the for Loop Example
Registers
R0: 5
R1: 3
R2: 3
STDIN:
STDOUT:
Console
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 0
…:
ML
Program Instructions
(N)
(i)
(SUM)
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R2 SUM * R2 is temporary sum
LOAD R1 #1 * R1 is i
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT

## Slide 24: Tracing the for Loop Example
Registers
R0: 5
R1: 3
R2: 3
STDIN:
STDOUT:
Console
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 0
…:
ML
Program Instructions
(N)
(i)
(SUM)
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R2 SUM * R2 is temporary sum
LOAD R1 #1 * R1 is i
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT
Notes: 3 <= 5
- True
- Back to top
- Do it again
- Make
- R2 3 + 3 = 6
- R1 3 + 1 = 4

## Slide 25: Tracing the for Loop Example
Registers
R0: 5
R1: 4
R2: 6
STDIN:
STDOUT:
Console
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 0
…:
ML
Program Instructions
(N)
(i)
(SUM)
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R2 SUM * R2 is temporary sum
LOAD R1 #1 * R1 is i
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT
Notes: 4 <= 5
- True
- Back to top and do it again
- Make
- R2 = 6 + 4 = 10
- R1 = 4 + 1 = 5

## Slide 26: Tracing the for Loop Example
Registers
R0: 5
R1: 5
R2: 10
STDIN:
STDOUT:
Console
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 0
…:
ML
Program Instructions
(N)
(i)
(SUM)
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R2 SUM * R2 is temporary sum
LOAD R1 #1 * R1 is i
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT
Notes: 5 <= 5
- True
- Back to top and do it again
- Make
- R2 = 10 + 5 = 15
- R1 = 5 + 1 = 6

## Slide 27: Tracing the for Loop Example
Registers
R0: 5
R1: 6
R2: 15
STDIN:
STDOUT:
Console
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 0
…:
ML
Program Instructions
(N)
(i)
(SUM)
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R2 SUM * R2 is temporary sum
LOAD R1 #1 * R1 is i
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT
Notes: 6 <= 5
- False….
- Don’t go to top… just continue

## Slide 28: Tracing the for Loop Example
Registers
R0: 5
R1: 6
R2: 15
STDIN:
STDOUT:
Console
15
Main Memory
0:
4:
…:
92:
96:
N 100: 5
SUM 104: 15
…:
ML
Program Instructions
(N)
(i)
(SUM)
N: .word
SUM: .word 0
LOAD R0 STDIN * Read n
STORE R0 N
* ...init...
LOAD R2 SUM * R2 is temporary sum
LOAD R1 #1 * R1 is i
JUMP COND
* ...loop body...
TOP: ADD R2 R2 R1 * sum = sum + i
* ...update...
ADD R1 R1 #1 * i++
COND: BLEQ R1 R0 TOP * i <= N
STORE R2 SUM
STORE R2 STDOUT
HALT
Notes: Put R2 into MM[SUM]
Display R2

## Slide 29: Acknowledgments
https://creativecommons.org/licenses/by/4.0/
Slide Template From:
Slide Content Licensed as:
Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.
Notes: Note: Individual images may be covered by their own licensing agreements and were incorporated here under fair use. Their use in this slide deck does not change or alter their licensing.

## Slide 30: The General the if Structure
Notes: This is the resource you’ll use in the activities.
It shows
- the HLL construct at the top (C)
- And the ASM structure at the bottom.
Very much the same as what we just saw.
- But it gives a template that can be used to build any of the different HLL structures.