## Slide 1: 04 - Logic Simplification
COMP 256 – Dickinson College
Prof. Braught
Spring 2022
Notes: Draw some gates and their logic expressions on the board for reference.
- AND, OR, NOT, NOR, NAND
First homework has been returned.
- Check Moodle
- Feedback file is your PDF marked up
- Checkmarks, comments
- Score and comment at the top
0,1,2 – Can resubmit within one week.
- 1 -> 2 : Only need to resubmit questions indicated in my comment
- 2 -> 3 : Look at checkmark scores and comments on enhanced questions.
Can just revise your original and resubmit.
Can create a new document just with revised questions
Up to you.

## Slide 2: Equivalent Circuits
Two circuits (or logic expressions) are equivalent if they compute the same Boolean function.
SOP
Notes: Last class we saw this circuit
- It computed the Boolean function represented by the truth table.
- If we look at that truth table we can generate an SOP expression for the function.
- Which gives us another way to build a circuit
- And that circuit uses less gates
- But computes the same function…
- So these circuits are equivalent…
This is just one example of equivalent circuits.
Sets the stage for what we will do today.

## Slide 3: Circuit Costs
Equivalent circuits compute the same function, but some may be better than others.
  Cost (roughly number of transistors)
  Speed (propagation delay)
2
4
6
Total Cost: 12
2
6
Total Cost: 8
Notes: The big idea is that if we have equivalent circuits, some may be “better” than others.
We know about NOT with 2 transistors.
Other gates (as we saw for NAND) have different circuits with different numbers of transistors.
These are the numbers for AND and NOR (google CMOS AND, CMOS NOR if you are interested)

## Slide 4: Circuit Costs
Equivalent circuits compute the same function, but some may be better than others.
  Cost (roughly number of transistors)
  Speed (propagation delay)
9ns
13ns
8ns
Total Delay: 21ns
9ns
13ns
Total Delay: 22ns
Notes: I looked them up for the 74HC series of CMOS chips that we will be using in the lab.
We won’t be concerned with finding propagation delays in this course,
But I want you to be familiar with the idea
And understand how it is related to logic simplification.
The important question becomes how do we find these simpler circuits?

## Slide 5: Boolean Identities and Equivalent Circuits
A Boolean identity is a rule that allows us to rewrite logical expressions into equivalent logical expressions, which may yield better (cheaper or faster) circuits.
Notes: For example consider this one identity…
Should look reasonably familiar from normal algebra.
- Factoring out the A.
So if we have say this circuit…
We can write its logic expression using our substitution method.
We can then apply the identity with A=Q, B=P and C=R to get an equivalent expression.
We can then turn that equivalent expression back into a circuit
And in this case, that circuit uses fewer gates and would be less expensive.
- Note: We didn’t reduce propagation delay – but we did reduce the cost.

## Slide 6: Boolean Identities
Identity
Null
Idempotent
Inverse
Commutative
Associative
Distributive
Absorption
NAND/NOR
DeMorgan’s
XOR
Double Negation
Name
AND Form
OR Form
XNOR
Notes: There are a good number of Boolean Identities.
You’ll get some experience with a few of these today and then more in the Activities.
The principle is the same…
- can rewrite an expression that looks like what’s on the left, with what’s on the right.
- or vice versa
- On the previous slide we used OR Form of Distributive Identity.
Again, the idea is that some expressions use fewer gates or fewer transistors or
give a circuit configuration with a smaller propagation delay or both.
You will study these identities and the Boolean Algebra more deeply in MATH 211.
For us, here they are purely practical ways to produce equivalent circuits.
This slide will be a useful reference.

## Slide 7: An Example:
Find a better equivalent circuit for the one shown below:
A
B
X
Notes: Work this one out on the board.
- Use substitution method to get a logic expression for the circuit.
- Find the Boolean Identity that applies
- Write it out & Label it with Name and Form
- Rewrite the expression for the circuit into its equivalent form.
- Draw the new circuit.
- Hummm… what does that mean?
- In this case, anywhere we needed X we can just run a wire from A!
- That’s better!
Can check your work with a truth table.
-

## Slide 8: An Example:
Find a better equivalent circuit for the one shown below:
A
B
X
A
X
Absorption AND
Tip: Use a truth table to double check your answers!
C
C
C X=AC
A B (A+B) X=A(A+B) X=A
0 0 0 0 0
0 1 1 0 0
1 0 1 1 1
1 1 1 1 1
Notes: This captures what was done on the board for later reference.

## Slide 9: Practice #1
Find an equivalent circuit for the one shown below but using fewer gates.
  Use substitution method to get a logic expression for the Boolean function W.
  Simplify W using a Boolean Identity.
    Indicate the identity and the form used.
  Draw the equivalent circuit.
  Check your work with a truth table.
P
Q
W
1.
2.
3.
4.
Notes: Work in pairs.
Comparing results with neighboring pairs.
We’ll cross check in a few minutes.

## Slide 10: Practice #1
Find an equivalent circuit for the one shown below but using fewer gates.
  Use substitution method to get a logic expression for the Boolean function W.
  Simplify W using a Boolean Identity.
    Indicate the identity and the form used.
  Draw the equivalent circuit.
  Check your work with a truth table.
P
Q
W
1.
2.
P
Q
W
3.
P Q P Q W=P+Q PQ W=PQ
0 0 1 1 1 0 1
0 1 1 0 1 0 1
1 0 0 1 1 0 1
1 1 0 0 0 1 0
4.
By DeMorgan’s AND Form ( )

## Slide 11: Practice #2
For each logic expression on the left apply the indicated Boolean Identity to rewrite it as an equivalent logic expression.
Absorption OR
Identity AND
Distributive OR
Distributive AND
DeMorgan’s AND
DeMorgan’s OR
Notes: Just apply the indicated identity once.
Don’t simplify any further.
Work in pairs.
Compare with neighboring pairs.
We’ll cross check in a few minutes.

## Slide 12: Practice #2
For each logic expression on the left apply the indicated Boolean Identity to rewrite it as an equivalent logic expression.
Absorption OR
Identity AND
Distributive OR
Distributive AND
DeMorgan’s AND
DeMorgan’s OR
Notes: 1. R takes the place of A and T takes the place of B in the identity.
2. Not X takes the place of A
3. AB Takes the place of A, C takes the place of B and Not D takes the place of C.
4. XY takes the place of A, W takes the place of B and Not W takes the place of C
5. Not A takes the place of A and DE takes the place of B
- Negate each and place them under the NAND – so NOT NOT A
6. NOT MN takes the place of A, P NOT Q R takes the place of B
Many of these could be simplified further if we were to apply additional identities.
Good follow up questions:
- Can we rewrite the NOT(MN) term as MN? Yes. Double negation.
- Can we rewrite the NOT( P NOT(Q) R) term as NOT(P)QNOT(R)?
- No. We would need to apply DeMorgan’s again.

## Slide 13: Practice #3
Use the Boolean identities to show that the circuit on the left can be simplified to the better equivalent on the right. Indicate the Boolean identity and its form used at each step of the simplification.
Distributive OR Form
DeMorgan’s AND Form x 2
Notes: Hint: I’ve given you the first two identities that I used.
- The x2 means that I used the identity twice in that step.
Can try on your own
Or the next slide shows all of the steps that I used to help you along.

## Slide 14: Practice #3
Use the Boolean identities to show that the circuit on the left can be simplified to the better equivalent on the right. Indicate the Boolean identity and its form used at each step of the simplification.
Commutative OR Form
Absorption OR Form
Idempotent AND Form
Double Negation x 2
Distributive OR Form x 2
Distributive OR Form
DeMorgan’s AND Form x 2
Commutative AND Form x 2
Idempotent AND Form x 2
Absorption OR Form

## Slide 15: Practice #3
Use the Boolean identities to show that the circuit on the left can be simplified to the better equivalent on the right. Indicate the Boolean identity and its form used at each step of the simplification.
Commutative OR Form
Absorption OR Form
Idempotent AND Form
Double Negation x 2
Distributive OR Form x 2
Distributive OR Form
DeMorgan’s AND Form x 2
Commutative AND Form x 2
Idempotent AND Form x 2
Absorption OR Form
Notes: Note: There are many other approaches that work.
Note: Often people will do the commutative and double negation steps with others.
- i.e. they “skip steps”
- If you do, just put both identities on the line.

## Slide 16: Integration Scale
Integrated circuits can be classified by the scale (i.e. magnitude) of Integration:
  Small Scale Integration (1-10 transistors/chip)
  Medium Scale Integration (10-100 transistors/chip)
  Large Scale Integration (100-1000 transistors/chip)
  Very Large Scale Integration (VLSI) (1000+ transistors/chip)
“AMD 2nd Gen EPYC Rome Processors Feature A Gargantuan 39.54 Billion Transistors”
  Oct 22, 2019
  https://wccftech.com/amd-2nd-gen-epyc-rome-iod-ccd-chipshots-39-billion-transistors/
Image from: https://www.nteinc.com/
integrated_circuits.php
Notes: Last class we talked about an integrated circuit.
There are different scales of integration…
Small - one or a few logic gates
Medium - would be like the even/odd detector from last class
Large – maybe some basic arithmetic
VLSI – full CPU on a chip
Today... Mind boggling.

## Slide 17: Moore’s Law
Gordon Moore, co-founder of Intel, observed in 1965 that the number of transistors on a silicon chip had approximately doubled every year and suggested that would continue for a decade.
  Later revised to every 24 months.
Graph from: https://www.ncbi.nlm.nih.gov/books/NBK321721/figure/oin_tutorial.F3/
Image from: https://www.sfgate.com/business/article/
Co-founder-of-Intel-honored-by-president-2798595.php
https://wccftech.com/
intels-3rd-generation-ivy-
bridge-core-i5-processor-pitted/
https://commons.wikimedia.org/
wiki/File:Intel_C4004.jpg
2300 Transistors
~40B Transistors
Notes: 10^9 = 1 billion
Vertical scale is log scale
So a straight line indicates an exponential relationship
- I.e. a periodic doubling of the value
- The slope would be indicative of 18-24 months.
So looks like we should be hitting 10^10 this year.
4004 -> 2300 (1971)
8086 -> 29,000 (1976)
5 years …. 2300, 4,600, 9,200, 18,400, 36,800
- so slightly under the line,

## Slide 18: Acknowledgments
https://creativecommons.org/licenses/by/4.0/
Slide Template From:
Slide Content Licensed as:
Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.
Notes: Note: Individual images may be covered by their own licensing agreements and were incorporated here under fair use. Their use in this slide deck does not change or alter their licensing.

## Slide 19
A Z
0 1
1 0
A
Z
A B Z
0 0 0
0 1 0
1 0 0
1 1 1
A
B
Z
A B Z
0 0 0
0 1 1
1 0 1
1 1 1
A
B
Z
A B Z
0 0 0
0 1 1
1 0 1
1 1 0
A
B
Z
A B Z
0 0 1
0 1 1
1 0 1
1 1 0
A
B
Z
A B Z
0 0 1
0 1 0
1 0 0
1 1 0
A
B
Z
A B Z
0 0 1
0 1 0
1 0 0
1 1 1
A
B
Z
NOT
AND
OR
XOR
NAND
NOR
XNOR
A B Z
0 0 1
0 1 0
1 0 0
1 1 0

## Slide 20
A
B
X
A
X
C
P
Q
W
P
Q
W
C X=AC
A B (A+B) X=A(A+B) X=A
0 0 0 0 0
0 1 1 0 0
1 0 1 1 1
1 1 1 1 1
P Q P Q W=P+Q PQ W=PQ
0 0 1 1 1 0 1
0 1 1 0 1 0 1
1 0 0 1 1 0 1
1 1 0 0 0 1 0

## Slide 21
A
B
Z
X
Q
P
R
P
R
Q
X

## Slide 22
P
Q
Z
P Q Z
0 0 1
0 1 1
1 0 0
1 1 1
P
Q
Z

## Slide 23: An Example

## Slide 24: Example: Simplify the expression
A
B
C
Distributive OR Form
Distributive OR Form
Notes: Let’s use the Boolean Identities to simplify this expression.
- I don’t expect you to to come up with the identities from thin air.
- you’ll have the reference sheet to use when working on the homework
When I compare the structure of Z to the identities
I find the right side of the Distributive OR form a match.
PQ term is A
Not P is B
Q is C
Then rewriting as it appears on the left.

## Slide 25: Example: Simplify the expression
Distributive OR Form
DeMorgan’s AND Form
A
B
DeMorgan’s AND Form
Notes: Doing the same thing
The PQ NAND term matches the right side of DeMorgan’s AND
A = P
B = NOT Q
Rewriting as on the left side.
Just doing it twice.

## Slide 26: Example: Simplify the expression
Distributive OR Form
DeMorgan’s AND Form
Distributive OR Form
Commutative AND Form
Notes: Here, it looks like I could use the Distribututive OR form
P+Q term = A
Not P = B
Q = C
Often there is more than one choice…
But we could also apply commutative AND form to each term.
No definitive rule for which one is better.
Just have to try them and see where they lead…
If things get worse, go back and try the other…

## Slide 27: Example: Simplify the expression
Commutative AND Form
Distributive OR Form
DeMorgan’s AND Form
Commutative AND Form
Notes: Let’s apply the Commutive AND form
Apply it twice
- to first term
- to second term

## Slide 28: Example: Simplify the expression
Distributive OR Form
DeMorgan’s AND Form
Distributive OR Form
Commutative AND Form
Distributive OR Form
Notes: Now we can use the Distributive OR form
Again – apply it twice here
- to first term
- to second term
Just like normal algebra.

## Slide 29: Example: Simplify the expression
Idempotent AND Form
Distributive OR Form
Distributive OR Form
DeMorgan’s AND Form
Commutative AND Form
Idempotent AND Form

## Slide 30: Example: Simplify the expression
Distributive OR Form
Distributive OR Form
DeMorgan’s AND Form
Commutative AND Form
Idempotent AND Form
Double Negation
Double Negation

## Slide 31: Example: Simplify the expression
Double Negation
Distributive OR Form
Distributive OR Form
DeMorgan’s AND Form
Commutative AND Form
Idempotent AND Form
Idempotent AND Form

## Slide 32: Example: Simplify the expression
Idempotent AND Form
Double Negation
Distributive OR Form
Distributive OR Form
DeMorgan’s AND Form
Commutative AND Form
Idempotent AND Form
Absorption OR Form
Absorption OR Form

## Slide 33: Example: Simplify the expression
Absorption OR Form
Idempotent AND Form
Double Negation
Distributive OR Form
Distributive OR Form
DeMorgan’s AND Form
Commutative AND Form
Idempotent AND Form
Commutative OR Form

## Slide 34: Example: Simplify the expression
Commutative OR Form
Absorption OR Form
Idempotent AND Form
Double Negation
Distributive OR Form
Distributive OR Form
DeMorgan’s AND Form
Commutative AND Form
Idempotent AND Form
Absorption OR Form

## Slide 35: Example: Simplify the expression
Commutative OR Form
Absorption OR Form
Idempotent AND Form
Double Negation
Distributive OR Form
Distributive OR Form
DeMorgan’s AND Form
Commutative AND Form
Idempotent AND Form
Absorption OR Form

## Slide 36: An Example
Notes: Faster and Cheaper.