## Slide 1: 09 – A Microprogrammed Machine
COMP 256 – Dickinson College
Prof. Braught
Spring 2022
Images from: openclipart.org

## Slide 2: Machine Abstractions
General purpose programmable computers can be understood as an abstraction hierarchy:
  Physical Machine
  Microprogram Machine
  Machine Language Machine
  Assembly Language Machine
  High-Level Language Machine
There are also several important architectural abstractions:
  The Stored Program Architecture
  The Instruction Cycle (Fetch/Decode/Execute)
  Memory Hierarchy & Cache
  Pipelining and Parallelism
Photo by: Steven Gerner, https://www.flickr.com/photos/sgerner/16477700444/in/photostream/
Used under a Creative Commons by-sa 2.0 license: https://creativecommons.org/licenses/by-sa/2.0/
Notes: Today we start a new unit on Machine Abstractions
- In a nutshell, how do we go from circuits to a general purpose programmable computer.
We get there through layers of abstraction in a hierarchy
- we have seen the physical machine
- from electrical voltages to 0-1, to transistors, go gates, to circuits,
- to the programmable circuit from lab that we instructed with 0’s and 1’s to perform different computations.
- In this unit we will look at
- A Microprogram machine
- A machine that is programmable with 0’s and 1’s that directly correspond to its configuration.
- A Machine language machine – still programming with 0’s and 1’s but at a higher level of abstraction
- Where the 0’s and 1’s will correspond to operations that we want to perform
- rather than how the machine is configured.
We will also see some higher level abstractions that capture important organizational (architectural) principles of how modern machines are built.

## Slide 3: Early Electronic Computers
Early electronic computers were not general purpose.
“Programming” required physical rewiring and setting knobs and switches to create a machine that performed the desired computational task.
Colossus – 1945
Tommy Flowers, Bletchley Park, UK
ENIAC – 1945
John Mauchly, J. Presper Eckert, Penn
Notes: I used the term “genera purpose programmable computer” on the previous slide.
I did that to differentiate from earlier computers that were not general purpose.
They were built or could be rewired to perform specific computations.
They could not be programmed to do different things.
If you wanted a different computation your reconfigured the machine physically.
That physical rewiring…
- Like building a bunch of circuits like in the lab
- where each circuit computes a particular set of functions (e.g. NOT, OR, AND, PLUS)
- each circuit was set each to perform the appropriate operation
- the output of each circuit was then connected to the inputs of the next
- to perform a sequence of operations
- i.e. a program.
Several of the earliest ones emerged at about the same time in the UK and the US.
You’ll have the opportunity to learn more about these machines and a few others in a video in the activities.

## Slide 4: The Knob and Switch Computer
Data Path
Registers (R0-R3)
Busses (A, B, C)
Arithmetic and Logic Unit
  ALU
Notes: We are going to work with The Knob & Switch Computer
- it is a model of a small computer
- organized based on the same principles as modern computers
- but let’s us see what is happening inside as it performs its computations.
- and allows us to interact with it directly.
- We will use it to build experience and intuition about how computers are organized and how they process information.
- Ultimately, it will help us understand how a computer can be programmed with 0’s and 1’s.
The main structure in the K&S is called the data path.
It consists of 3 main elements:
- Registers: Temporary storage for values used in the machine’s calculations
- Busses: wires that connect the different components and allow the electrical signals to move between them.
- ALU: Performs the actual computations

## Slide 5: The Knob and Switch Computer Datapath
DEMO!
https://dickinson-comp256.github.io/Knob-And-Switch-Computer/datapath.html
Notes: Short demo of how the K&S data path works and how we can interact with it.
Type in some values
- use small positive and negative values
- make positives checkable by hand
Click some knobs to choose registers and operations.
Setup and execute an operation:
- R2 = R0 + R1
- Talk through the animation.
- Change the animation speed.
Change to Base 2 and check values.
- (+-10 uses Two’s complement representation)

## Slide 6: Try It!
Multiply the value of a register by 2 and place the value in another register.
Assuming all registers have a non-zero value, set one register’s value to 0.
Replace the value in a register with its complement (e.g. replace -235 with 235). Your solution should work regardless of what is in the other registers.
Multiply the value in a register by 7. Use as few steps as possible.
https://dickinson-comp256.github.io/Knob-And-Switch-Computer/datapath.html
Work in pairs to use the settings in the Knob & Switch Datapath to perform these tasks.
Notes: Work on these for a little while.
Have a report out on ideas and questions.
Leave enough time to cover the rest of the materials.

## Slide 7: Knob and Switch Computer with Main Memory
Main Memory (RAM)
Memory Locations
  16-bit values
  32 locations
    5-bit addresses
    Unsigned binary
Switches
Notes: In the homework you will work with two more versions of the K&S computer.
Each adds a little more complexity and a little more power.
The first of these two is the K&S with Main Memory.
The big change is that we’ve added a Main Memory:
- The 4 Storage locations provided by the registers are not much.
- The Main Memory holds more data
- When you talk about the RAM in your computer it is the Main Memory that you are talking about.
- K&S’s Main Memory is pretty small (32 locations)
- compared to the 4, 8, 16 + GB that you have.
- A giga is about 1 billion so 4, 8 or 16 billion locations
- But the idea is exactly the same.
Every location in the K&S
- holds 16 bits.
- has an address so that we can refer to it.
- addresses are 5-bits long in unsigned binary
- Can also see in base 10.
We use the switches to change how data moves.
- move from registers to registers (as before)
- Move from memory to registers
- Move from registers to memory (thorugh the ALU)
Be careful not to connect two inputs to C-Bus at the same time.
- Data collision – bad news… corrupted results.

## Slide 8: Programming the K&S?
How might we create a program for the K&S using only 1’s and 0’s?
Notes: Do a little brainstorming.
No need to get it exactly right.
The details come out in the homework.

## Slide 9
Microinstructions are an abstraction for the machine configuration.
  0’s and 1’s encode knob and switch positions.
A micro-program is a sequence of micro-instructions.
The Knob and Switch Computer (v3)
Notes: Now we can think about programming the machine using 1’s and 0’s instead of switches and knobs.
- we just need to agree on a way to encode
- the position of each knob
- the state of each switch
- the memory location to be used.
Once we agree on that, we can write down machine configurations as a series of 1’s and 0’s.
Write down a sequence of those configurations
Execute them one after the other and we have a program!
(Set one up in advance and run it just to see it go)

## Slide 10: Acknowledgments
https://creativecommons.org/licenses/by/4.0/
Slide Template From:
Slide Content Licensed as:
Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.

## Slide 11: The Knob and Switch Computer (v1)
Data Path
Registers (R0-R3)
Busses (A, B, C)
Arithmetic and Logic Unit
  ALU
Number Base
Notes: Can display the contents of the machine in a variety of different representations.

## Slide 12: The Knob and Switch Computer (v1)
Data Path
Registers (R0-R3)
  16 bit values (word size)
Busses (A, B, C)
Arithmetic and Logic Unit
  ALU
Number Base
  +- 10 (Two’s Complement)
  10 (Unsigned Binary)
  2 (Show the bits)
Notes: See that Registers hold 16 bits:
- 16 bits vs 64 bit machine
The