## Slide 1: 26 - Threads
COMP 256 – Dickinson College
Prof. Braught
Spring 2022

## Slide 2: Process Review
A program is a list of instructions.
  Static
    Just the code & data segments
A process is a program that is in a state of execution.
  Dynamic
    Heap, Stack, Registers, PC
    Process context
      All of the information that would be needed to suspend the process (“deep freeze it”) and then restart (”thaw”) it right where it left off.
PC:76
Registers
R0:20
R1:141
R2:12
R3:0
…
R14:141
Page Table
CPU
Empty
0:
2m-1:
ML
Data
Stack
Logical Memory
Heap
Notes: This is review of what we learned about programs and processes.
Recall:
- A program is just the instructions and global data.
- The program is not running.
- So it is static:
- Its variables do not have values, there is no current point of execution.
- It has no values in registers, it is not even in memory.
- A process is a program that is currently in a state of execution.
- It has been loaded into memory
- Its variables have values.
- It has specific values in registers
- There is a specific point at which it is executing (i.e. a PC value or a current instruction).
The process has a context
- That context is all of the dynamic information
- It is what needs to be saved or restored when we context switch from or to this process.

## Slide 3: A Thread of Execution
A context captures the state of a process at a point in time, and over time it traces a Thread of Execution through the program.
PC:76
Registers
R0:20
R1:141
R2:12
R3:0
…
R14:141
Page Table
CPU
Program at: https://repl.it/@braughtg/MainThreadEx
Notes: Consider the program….
When running the program is a process
- it has a context
As the program executes
- The context will change
- The PC will change
- The variable i will be created on the stack
- The PC will change and the machine will fetch/decode/execute
- The registers will change
That changing context ”Traces a thread of execution” through the program.
Note: The context shown in the CPU box don’t change because I just haven’t animated that.
- but those things would clearly change as the program executes.

## Slide 4: Multiple Threads of Execution
Having multiple contexts allows multiple threads of execution within a single process.
Program at: https://repl.it/@braughtg/TwoThreads
Each instance of the Thread class creates a new execution context for the run() method when the start() method is called.
Notes: This is the same program as before with a few added statements.
The statement new PrintIt creates new object that is sub-class of Thread
- Thread is class provided by Java.
- The thread class contains a method named run() that we override.
Calling start() on a Thread
- creates a new execution context
- That context will execute the run() method that is defined in the Thread.
- Creating a new execution context is similar to creating a new process.
- It is done via a system call to the OS
- That is, the code in the start() method makes a system call.
- But a whole process is not created:
- because the Thread is in the same program, its code and data are already loaded into memory.
- And the OS already has a PCB for the process.
- But some additional information will be needed and we’ll get to that in a little bit.
Run the program here and observe the output that it generates.
- what can we notice about the different outputs?

## Slide 5: Multiple Threads of Execution
Having multiple contexts allows multiple threads of execution within a single process.
Program at: https://repl.it/@braughtg/TwoThreads
Run this program multiple times. What do you notice about the outputs?
Notes: Collect some observations…

## Slide 6: Multiple Threads of Execution
Having multiple contexts allows multiple threads of execution within a single process.
Program at: https://repl.it/@braughtg/TwoThreads
Assume that independent threads may execute in any order, unless we force them to do otherwise.
Notes: What we are seeing in the is the independent execution contexts of the main thread and the PrintIt thread.
We may notice that:
- The line “Hi I’m Main” is always first.
- This is because the PrintIt thread has not yet been started and the main thread is the only one able to run.
- After the PrintIt thread is started there will be two threads that are ready to run.
- The OS will then use multiprogramming to switch back and forth between them.
- The scheduler will move these execution contexts (i.e. threads) from the ready state to the running state and back.
- The order in which these switches happen is operating system and circumstance dependent.
Tip: When running multiple threads, it is best to assume that the instructions can run in any order.
- We will see later that we can impose an order if it is important to us.

## Slide 7: Multiple Threads of Execution
Having multiple contexts allows multiple threads of execution within a single process.
Hi I'm Main
0: Main
1: Main
2: Main
3: Main
0: It
1: It
2: It
3: It
4: It
4: Main
Main done!
Program at: https://repl.it/@braughtg/TwoThreads
Notes: Let’s look in more detail at the execution of our multi threaded program.
- When the process starts
- The main thread is the only execution context (represented by the green dot)
- main will eventually be selected by the OS scheduler to run
- When that happens, main’s context is switched onto the CPU
- The green dot traces out main’s thread of execution (the red line)
- main prints “Hi I’m Main”
- main then makes a system call to create a new thread of execution for PrintIt.
- PrintIt it gets its own context (represented by the blue dot)
- That dot will trace out the thread of execution for the thread
- main makes a system call to start the thread t1
- This just causes t1 to be put into the ready queue
- main might continue to run a little while longer because it’s time slice is not up yet
- in this case we assume that main prints out its 0 and 1 lines
- When main’s time slice is up
- OS does context switch and we’ll assume that it schedules the thread t1 to run
- t1s thread will run – the blue dot will trace out t1’s thread of execution (blue line)
- here t1 prints out its 0 and 1 lines
- When t1’s time slice is up
- OS will again context switch, and we’ll assume main is selected to run
- Though there could be others from other processes that run in between.
- In this time slice, main prints its 2 and 3 lines
- When main’s time slice is up
- The OS will again OS context switch, and we’ll assume it picks t1
- again possibly with other processes in between)
- t1 this time prints its 2, 3 and 4 lines
- t1 then reaches its end and makes a system call to terminates
- OS context switches again, we’ll assume it picks main
- main prints its 4 and done lines.
- the Main thread reaches its end and makes a system call to terminate.
- Because main is the last thread in the process this also terminates the process.
Notice similarities to some of the different orderings that we saw when running the program.
- This is not the only possible order.
- There are lots of them.

## Slide 8: The OS View: Managing / Context Switching Threads
Process Context (PCB):
  Shared by threads:
    Program/Data/Heap
    Page Table
    Files / devices
Thread Context (TCB):
  Each thread has:
    PC
    Registers
    Stack
PID:139
Proc Info:
Files:
Threads:
main
PrintIt
Page Table
PCB
PC:76
Registers
R0:20
R1:141
R2:12
R3:0
…
R14:141
TCB:main
PC:893
Registers
R0:3
R1:5
R2:75
R3:0
…
R14:19
TCB:PrintIt
Empty
0:
2m-1:
ML
Data
main:Stack
Logical Memory
Heap
Empty
it:Stack
Notes: How does that all work at the internal OS level?
Basically, each PCB now will have a Thread Control Block (TCB)
- The PCB holds all of the information that is common to all threads in the process.
- Eg. A Process Identifier (PID)
- The page table for mapping virtual addresses to physical addresses.
- Information about files the process has open
- Links to a Thread Control Block for each thread.
- The TCB for a thread holds the individual context for that thread of execution.
- PC: Which instruction is it executing
- The register values for that execution context.
- This is really just like we were thinking about the different processes up until this point.
- It is just that threads share some stuff.
- The program/data/heap segments, a logical memory space, etc.
- So now we would think about the TCB’s as what is being moved between the states instead of TCBs
- e.g. Ready / Running / Wating / etc.

## Slide 9: The Metaphor
College Metaphor
Hardware:
rooms, equipment
Program:
class, team, student
OS:
faculty, staff, coaches
Notes: A class may have multiple groups working independently on an activity
- If the class is a process then each each group is like a thread
- each group is executing the same program – i.e. the activity
- but each group may be working at a different pace, so may be at a different point in the activity
- One group may be running the code in the function “question #1”
- While another is running in the function “question #3”
- This is like the main thread and the PrintIt threads.
- Or each group could be working on different data
- They might all be running the “question #1” function
- But each group may be using different values in their computations.
- This would be like having multiple copies of the PrintIt thread running.
- Each one may be at a different palace with different register / local variable values / different parameters
Faculty as the OS will coordinate the groups
- maybe calling on each to report out in turn
- maybe letting each use the whiteboard in turn
- This is like the timesharing and scheduling.
Notice that each thread has its own copies of some resources:
- Registers, stack, PC, etc…
- Like the activity sheet and the point at which they are working.
But other things are shared across threads (i.e. one for the whole process) - activity (program & data segment)
- Like the classroom, whiteboard etc.
- They are the hardware that is owned by the process, shared by the threads
- I.e. one for the whole class and shared by the groups.

## Slide 10: Waiting for a Thread
Thread.join()
  The calling thread (main here) waits for the thread on which join is invoked (t1 here) to complete.
main will pause here and wait for t1 to complete
Program at: https://replit.com/@braughtg/ThreadJoin
Notes: The Thread class defines a method name join.
- When join is called on a thread
- the thread that calls it pauses and waits for the thread on which join is called to complete.
- So here main has called join on thread t1.
- Thus, the main thread will pause and wait for t1 to complete.
The effect in this case will be that the line “Main done!” will never be printed before t1 completes.
- So “Main done!” will always be the last thing that is printed.
If there is time, open it in repl and run it a few times.

## Slide 11: Common Thread use Patterns
Parallelization
  Multiple threads all concurrently performing the same computation but on different parts of the data.
Specialization
  Multiple threads each concurrently performing a different computation on the the same or different parts of the data.
Notes: Parallelization:
- Compute the total of all of the values in an array.
- Divide the array into chunks
- Use a separate thread to compute the total of each chunk.
- Sum those totals together at the end.
- This is also what happens in your browser when you open multiple tabs.
- Each tab is performing the same computation
- Loading and displaying a web page.
- The data is different
- The page being loaded and displayed is different.
- Web servers do something similar
- Every request that comes in for a page is handled by a thread.
- That thread goes and gets the requested page and returns its.
- Same computation, different data.
Specialization:
- Find the max and min and average of an array.
- Use separate threads for finding the max, the min and the average.
- Each thread processes the entire array.
- But each thread does a different computation.
- Your web browser may also do this.
- Once tabs are loaded what is happening in those tabs may be different.
- One may be playing video
- Another may be showing a static HTML page
- Another may be running a webapp that is waiting for you interact with it.
- Different threads each doing something different.

## Slide 12: Acknowledgments
https://creativecommons.org/licenses/by/4.0/
Slide Template From:
Slide Content Licensed as:
Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.
Notes: Note: Individual images may be covered by their own licensing agreements and were incorporated here under fair use. Their use in this slide deck does not change or alter their licensing.