## Slide 1: 13 – Pipelining & Parallelism
COMP 256 – Dickinson College
Prof. Braught
Spring 2022

## Slide 2: Stored Program Architecture
The stored program architecture with memory hierarchy and processor cache.
Notes: Last class we looked at the memory hierarchy
That included large, slower, cheaper storage on I/O devices
- Solid State Drives (SSD)
- Hard Disk Drive (HDD)
- Optical Drives
- Tape backup
It also included smaller, faster more expensive memories
- Main memory (DRAM)
- Cache and CPU Registers (SRAM)

## Slide 3: Performance Improvements
Moore’s Law → More Transistors
Better Designs
  Processor Caching
  Pipelining & Parallelism
Better Software
  COMP232, COMP332
Notes: So, caching was about getting information to the processor with less delay
Recall that processors got faster more quickly than did memory
So CPU would have been sitting idle waiting for data.
Cache memory makes it possible to get data to the CPU faster at a reasonable cost.
Today’s topic…
Pipelining and Parallelism are both about making the processor even faster
- Well really more about having it do multiple things at the same time
- Thus, getting more done per unit of time
- Even if none of those individual things are any faster.

## Slide 4
You have 4 loads of laundry to wash, dry and fold. You have 1 washer and one dryer. Each step takes 20 minutes. What is the fastest way to get all of the laundry done? How long does it take?
Image adapted from: http://www.cs.iit.edu/~cs561/cs350/piplining/laundry.html
with Images from: openclipart.org
Notes: I know how college is…
- This is a public service announcement… ;)

## Slide 5: A Pipelining Metaphor
W
D
F
F
D
E
F
D
E
F
D
E
F
D
E
Program
Instructions
Loads of
Laundry
20
20
20
20
20
20
20
20
20
20
20
20
Image adapted from: http://www.cs.iit.edu/~cs561/cs350/piplining/laundry.html
with Images from: openclipart.org
Notes: Here’ we will use another metaphor…
Imagine you have 4 loads of laundry to do.
- Starting with load A,
- wash (20 minutes)
- dry (20 minutes)
- fold (20 minutes)
- Then we could do load B
- Then C and D and by Midnight you’d be finished with your laundry.
- Of course that’s not how you would do your laundry right?
But that it is exactly the way we have been talking about the instruction cycle of the computer
- Replace WDF with FDE and we have the instruction cycle.
- Just like it doesn’t make sense to let the washer sit there doing nothing while we were drying and folding
- It doesn’t make sense to let the hardware for Fetch just sit there while we decode and execute.
So, let’s do with the instruction cycle what you do with your laundry.

## Slide 6: A Better Solution
F
D
E
F
D
E
F
D
E
F
D
E
Program
Instructions
Loads of
Laundry
20
20
20
20
20
20
20
20
20
20
20
20
Image adapted from: http://www.cs.iit.edu/~cs561/cs350/piplining/laundry.html
with Images from: openclipart.org
Notes: Because each step uses distinct hardware (Washer, Dryer, Folding Area)
- we can overlap them in time.
- While drying the first load, we can wash the second load.
- While folding the first load, we can dry the second and wash the third.
- Or in terms of an instruction, we execute the first one, while decoding the second one, while fetching the first one.
We finish in half the time!
So even though none of the pieces got any faster, we got more done per unit of time
So, if someone is just looking at how long it takes to do laundry
- It seems like the ”Laundry doing machine” is now twice as fast as it was.
- We can imagine a laundry service here as an abstraction…
- You hand off your clothes and pay (relevant detail)
- They come back clean, dry and folded (relevant detail)
- Doesn’t matter which process they use internally to get that done (hidden detail)
- We can do the same with our processor…
- We give it a list of instructions to execute
- It gives us back the result
- We don’t care how it does it
- so the processor provides an abstraction
- that may be hiding pipelining
- which allows it to do its job much faster without us worrying about it at all.
One critical point
- At any given time we are using a piece of hardware for only one thing.
- Washer, dryer, folding table.
- Not trying to use the same washer for two different loads at the same time.
- Colors bleed and whites turn pink.
- Or instructions and data get corrupted.

## Slide 7: Instruction Cycle Pipelining
A pipelined instruction cycle overlaps the stages of the cycle (e.g. Fetch / Decode / Execute) by using independent hardware components in each stage.
  Pipeline Hazards are conditions that prevent the the instruction pipeline from operating at maximum efficiency.
Image from: openclipart.org
Notes: Just a definition of pipelined instruction cycle.
- Worth note that the cycle is typically broken into more stages in practice.
- Pentium 4 had 20 stages
- Newer pentium processors up to 31 stages
- Just break it down into smaller and smaller stages
- Fetch: might become request, retrieve, store
- Decode: might have multiple steps
- Execute: might become
- get data from registers
- do the alu op
- store result back to registers
Pipeline hazards are things that come up that cause things to not work perfectly.
- Painted kind of a rosy picture of FDE all nicely overlapped.
- Turns out there are some things that will mess that up.

## Slide 8: Pipeline Hazards
R0←MM[25]
IR←MM[PC]
What issue arises with the pipelined instruction cycle in the situation shown here?
How might it be addressed?
Notes: Here we have a pipelined instruction cycle
- Fetch the first instruction
- Decode it while fetching the second instruction
- Execute it while decoding the second instruction and fetching the third instruction
- And so on…
Let’s imagine that first instruction moves a value from MM to a register
- R0 <- MM[25]
But then notice that fetching the 3rd instruction requires the use of MM also!
- IR <- MM[PC]
This is a resource hazard
- The execute and the fetch both need to use MM at the same time.
- But just like we can’t wash colored clothes and white clothes in the same machine at the same time
- We can’t access MM[25] and MM[PC] at the same time.

## Slide 9: Resource Hazards
A resource hazard occurs when two pipeline stages require the same hardware at the same time.
  E.g. Fetch and Execute may both need to access main memory at the same time.
R0←MM[25]
IR←MM[PC]
Notes: Here we have a pipelined instruction cycle
- Fetch the first instruction
- Decode it while fetching the second instruction
- Execute it while decoding the second instruction and fetching the third instruction
- And so on…
Let’s imagine that first instruction moves a value from MM to a register
- R0 <- MM[25]
But then notice that fetching the 3rd instruction requires the use of MM also!
- IR <- MM[PC]
This is a resource hazard
- The execute and the fetch both need to use MM at the same time.
- But just like we can’t wash colored clothes and white clothes in the same machine at the same time
- We can’t access MM[25] and MM[PC] at the same time.

## Slide 10: Pipeline Bubbles
Inserting a bubble into the pipeline is one technique that can be used to resolve a hazard.
R0←MM[25]
R2←R0+R1
Pipeline
Bubble
(NOP)
IR←MM[PC]
Notes: So one way to deal with hazards is to insert a bubble.
For example
- We insert a bubble where we would have fetched the third instruction.
- The bubble is essentially a NOP instruction that does nothing (uses no hardware)
-The conflicting fetch is then shifted one time slot to the right
- Thus, it no longer conflicts with the execution of the first instruction.
- So, as long as the execution of the second instruction doesn’t use MM everything is okay.
- E.g. it could add two registers.

## Slide 11: Control Hazards
A control hazard occurs when a branch causes instructions that have already been fetched to not be executed.
PC←7
IR←MM[15]
IR←MM[16]
PC=14,
IR←MM[14]
Branch 7
Notes: If the PC = 14 then the next instruction is fetched from MM[14]
It is then decoded
- imagine it is an unconditional branch to address 7
- while that is being decoded the next instruction is being fetched
- From address 15
- We know that isn’t right, but the computer doesn’t yet
- Because it hasn’t been decoded, yet alone executed.
- So it just carries on as if the the next instruction would be at address 15.
Then the branch is executed and the PC is changed to 7.
- but in the meantime the control unit has
- decoded the instruction at MM[15]
- fetched the instruction at MM[16]

## Slide 12: Control Hazards
A control hazard occurs when a branch causes instructions that have already been fetched to not be executed.
  Decoding and execution of incorrect instructions is canceled.
PC←7
(branch)
IR←MM[7]
X
X
X
Notes: So once the machine hardware recognizes that
- It has fetched and decoded incorrect instructions
- it cancels further processing of them.
Then the next fetch
- Comes from the correct location MM[7] because the branch has executed
- The PC has been changed.
[Maybe mention depending upon time]
Because nothing in the incorrect instructions has been executed
- There is no issue once they are canceled.
- In more complex pipelines, sometimes these instructions will have changed something before they are canceled.
- In that case, in addition to canceling further processing
- anything that has been done has to be undone.
- More complex, but overall still an improvement in performance.

## Slide 13: Super Scalar Processors
A Super-Scalar Processor has multiple functional units (e.g. ALUs).
  Multiple instructions are fetched at the same time.
  Instructions are matched to the available functional units during decoding.
  Multiple instructions are executed in parallel.
  Results are put back into order by a “commit unit”
Notes: Some of those 4-billion transistors are used to build more ALU’s
- Like adding more washing machines and more dryers.
Because each functional unit can execute an instruction
- We will need multiple instructions for each execute phase.
Fetch:
- Build the hardware so that it fetches multiple Instructions at at time.
- Uses multiple instruction registers (IR)
- Also possibly multiple program counters (PC)
- So instructions may even come from different programs.
Decode:
- The machine figures out what each instruction is
- Matches each instruction to an appropriate functional unit
- imagine small and large washing machines for small and large loads
Execute:
- Each functional unit processes its instruction in parallel with the others
- all washers (small and large) work at the same time.
Commit:
- Reorder the results so that they are back in the correct order.
- hides the fact that they were done all at the same time.
- All the wash gets folded and put back in the right drawers
Like with pipelining
- There can be dependency issues that limit the maximum benefit.
- For example:
- x = y + 2
- y = x +4.5
- We could not do these two operations in parallel.
- Why not?

## Slide 14: Multicore Processors
A multicore processor has multiple complete CPU cores on a single processor chip.
  Each core is super-scalar and pipelined
  Cores can execute:
    different programs
    different parts of same program
Multiple levels of cache.
  Shared L3 cache
  Per Core L2 and L1 cache
    Separate L1 caches for data and instructions.
Image adapted from: https://www.enterpriseai.news/2014/07/09/
Shared-memory-clusters-numa-cache-latencies/
L1 Data Cache
L1 Data Cache
L1 Inst Cache
L1 Inst Cache
Main Memory
Input/ Output
Notes: Multi-Level cache works in stages:
- Check the appropriate L1 cache for the data or instruction.
- If there is a hit use the returned value.
- done
- If not then check the L2 cache
- If there is a hit use the returned value
- and copy it and the nearby stuff to the L1 cache.
- done
- If not then check the L3 cache
- If there is a hit then use the returned value
- and copy it and the nearby stuff to the L2 and L1 caches.
- done
- If not then retrieve the data or instruction from main memory
- Use the returned value
- and copy it and the nearby stuff to the L3, L2 and L1 caches.
- done
- One optimization that can be made
- Issue the request for the data to all cache levels and MM at the same time.
- Then if there is a hit, cancel the request at any of the slower levels.

## Slide 15
Why might it be an advantage to have separate Data and Instruction caches for each core?
Image adapted from: https://www.enterpriseai.news/2014/07/09/
Shared-memory-clusters-numa-cache-latencies/
L1 Data Cache
L1 Data Cache
L1 Inst Cache
L1 Inst Cache
Main Memory
Input/ Output
Notes: Hints:
- Locality of references
- Resource hazards

## Slide 16
What issues might arise with writing data changes to main memory in a system with multiple cores where each has its own cache?
Image adapted from: https://www.enterpriseai.news/2014/07/09/
Shared-memory-clusters-numa-cache-latencies/
L1 Data Cache
L1 Data Cache
L1 Inst Cache
L1 Inst Cache
Main Memory
Input/ Output
Notes: Hint:
- There may be multiple copies of the data.
- Which get’s updated?
- What would be fastest?
- What problems might arise?
Any ideas on how that issue could be addressed?

## Slide 17: Speedup
The speedup of an improvement is:
Derive an equation that gives the maximum possible speedup due to an instruction pipeline as a function of the number of stages (k) and the number of instructions (n)
Notes: For example:
- if the time taken for the improved version is ½ the original
- then the speedup S = 2.
Hints:
- Assume each stage takes 1 time unit.
- Write an expression for the time to complete n instructions without overlapping the stages.
- I.e. doing your wash the slow way.
- That is Time Original
- Write an expression for the time to complete n instructions with overlapping (i.e. pipelining).
- I.e. doing your wash the fast way.
- That is Time Improved.
Hints:
- Figure it out Time original and Time improved for the wash example.
- Does your formula give the same result?
Now, can you simplify your formula if you assume the number of instructions is very large?

## Slide 18: Acknowledgments
https://creativecommons.org/licenses/by/4.0/
Slide Template From:
Slide Content Licensed as:
Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.
Notes: Note: Individual images may be covered by their own licensing agreements and were incorporated here under fair use. Their use in this slide deck does not change or alter their licensing.

## Slide 19
CPU
Main
Memory
Input/ Output
REG

## Slide 20
F
D
E
F
D
E
F
D
E
F
D
E
Program
Instructions
20
20
20
20
20
20
20
20
20
20
20
20
F
D
E
Notes: Because each step uses distinct hardware (Washer, Dryer, Folding Area)
- we can overlap them in time.
- While drying the first load, we can wash the second load.
- While folding the first load, we can dry the second and wash the third.
- Or in terms of an instruction, we execute the first one, while decoding the second one, while fetching the first one.
Finish in half the time.
Important piece is that at any given time we are using a piece of hardware for only one thing.
- Washer, dryer, folding table.
- Not trying to use the same washer for two different loads at the same time.
- Colors bleed and whites turn pink.
- Or instructions and data get corrupted.

## Slide 21
Fetch
Decode
Execute
Commit